CSL as an abstract modeling language, compliments the Electronic System Level design (ESL) process. By using a high level language with the expressiveness of standard
RTL and the power of a second generation RTL language, The CSL language is object oriented. The CSLC tool meets your design team’s needs in many ways. Examples include reduced time to a completed design interconnect, reduced time to C/C++ an RTL test, reduced consistency bugs due to interface or constant value differences, and reduced bugs due to bugs in commonly coded modules..
automatically generate module with correct interfaces
automatically generate common components
automatically generate a memory map with no address collisions
automatically generate a memory map connected to state elements (registers and registers file and SRAMs)

Reduced Bugs Introduced into the Downstream Flow
The CSLC tool helps prevent undetected bugs from being
introduced into the design database via the specification
 Fastpath Logic®
C/C++ and RTL front end chip design specification, code generation, visualization, and design analysis SOLUTION DATASHEET
CSLC®

The Front End RTL Design and Verification Productivity Solution

activities need to be minimized. Examples of non-value added
activities include test bench construction, constant
generation, interconnect design and implementation.

The CSLC Method
Front end RTL design tasks are automated in the CSLC software. The CSLC software facilitates rapid design database changes. Modules can be added or deleted and interfaces can be modified easily. The same design database can be used for multiple projects simultaneously by employing the CSLC tool to add and subtract object features. The CSLC tool facilitates incremental design techniques, intellectual property integration, system on chip design, and rapid verification environment construction.

The CSL language combines a high level object oriented language with the expressiveness of standard RTL and the power of a second generation RTL language.
The CSLC tool meets your design team’s needs in many ways - it improves time to a completed design interconnect, reduces time to C/C++ and RTL test, decreases the bug count in commonly coded modules and reduces the consistency bugs due to interface or constant value differences.

<added>
CSL design patterns are equivalent to C++ design patterns. CSL is a high level compiler, analyzer, RTL/C++ code generator, design component generator, report generator.
A pattern is insert wikipedia definition here
Software patterns were recognized in programming languages and were developed 20 years ago. There are also RTL/hardware design patterns; the common RTL/hardware design patterns are used by CSL. Common patterns are found in hardware design and in verification environments.
Using the same high level specification language (CSL) the cslc will generate consistent interfaces between software verification components and hardware design components, consistent interfaces between hardware design units, consistent constants for both the C++ and RTL code bases.
</added>
As Designs continue increase in complexity and design times decrease, new methods for reducing schedule times are necessary. Moreover, as design budgets decrease, the manpower required to build new products increases compared to previous projects. The number of transistors on ASIC’s and custom VLSI chips is estimated to increase 100x from 2005 to 2015. Current design methodologies will not be able to keep pace with the continuing increase in design
complexity and shorter times to market. Clearly a change in
design methodologies is required. Non value added

Figure 2 Front end RTL/C++ code generation flow

 language, the analysis engine, and the code generators. This leads (among other things) to a reduced number of bugs which translates directly into a schedule saving.

Interconnect Generation
The CSLC tool reads the CSL interconnect specification and produces the design hierarchy and the connections between modules in the design hierarchy. Signals need not to be specified between two end points. An auto router will automatically connect the two or more end points. The use of the auto router in CSLC specifications allows design teams to rapidly change hierarchies. This practice has been beneficial to projects which discovered problems during the floor planning stage.

Test Vector and Generation
The CSLC tool reads the vector specification which groups signals together specified in the CSL interconnect
specification and associates the signals with a vector name, clock domain, reset signal, the event used to capture the
vectors, and the max number of vectors,… Vectors are
generated by C/C++ simulators. Vectors are used for verification purposes by test benches.

Architectural Test State Generation
The CSLC tool reads the architectural test state specification which associates a single aggregate state element (register file, FIFO, SRAM,…) specified in the CSL specification and associates the state element with an architectural test state name, the event used to capture the
state, clock domain, reset signal, the maximum number of frames (snap shots of the state element at various times. The state is generated by C/C++ simulators. State is used for verification purposes by test benches.

Test bench Generation
The CSLC tool will automatically generate test benches for each module in the design. The design under test can be driven with test vectors which are either loaded and written on a file and into a memory or transmitted to the test bench through a PLI socket. The output test vectors are compared to the output of the design under test. The test benches also can load architectural state and compare it to the design under test architectural state. Counters track the number of matches and mismatches.

Memory map generation
The CSLC tool can generate the memory map for a chip design from a CSL memory map specification. The CSLC will generate the C/C++ and RTL constants which represent the memory addresses of specific elements in the design as well as address range checkers and decoders.
Figure 1 CSLC inputs and outputs

way, designers avoid common coding errors.

Pipeline generation
The CSLC tool will generate the C/C++ and RTL pipeline implementations for a chip design from a CSL pipeline specification. Complex pipelined and parallel pipelined registers can be connected to signals with pipe stage suffixes using the CSLC interconnect specification in conjunction with the CSL pipeline specification. Pipe stages are checked for correct connections and pipelines are checked for correct latencies using the CSLC analysis engine.
Defining common interfaces in the design and verification components
Design and verification components have common interfaces. The common interfaces are used to communicate between different models and to compare vector and state values at various intervals. Vectors and states are assigned names for the purposes of selecting the vectors and states. Vector and state names are commonly used in documentation, C++ model vectors, test bench vector readers and writers, regression scripts, and test lists.
Register generation
The CSLC tool will generate the C/C++ and RTL register implementations for a chip design from a CSL register specification. Registers can be associated with addresses from the CSLC memory map specification, thus avoiding coding errors. Different types of registers (counter, interrupt, ...) can be generated which avoids common coding errors by designers. Registers can be connected to signals using the CSLC interconnect specification.

Register File generation
The CSLC tool will generate the C/C++ and RTL register file implementations for a chip design from a CSL register file specification. Register files with the addresses from the CSLC memory mao specification leads to avoiding coding errors. Different register file personalities can be generated thus avoiding common coding errors by designers.

Fifo generation
The CSLC tool will generate the C/C++ and RTL FIFO implementations for a chip design from a CSL FIFO specification. FIFO’s can be combined with addresses from the CSLC memory map specification in order avoid coding
errors. Different FIFO personalities can be generated. In this
CSLC Features and Benefits
The table below describes the CSLC features and benefits and the competitions to corresponding competing features. It is difficult to find competing features for some CSLC features since nothing as comprehensive as CSLC has been offered commercially yet.

CSLC Features	Benefits	Standard competing feature
Able to read pre-existing designs and CSL specifications into the same object model and check the combined designs	Perform the static verifications so that the pre-existing RTL files and the CSL specification files “work” together.	In house connectivity tools, it can read designs but are normally unable to check designs. Instead RTL code is generated and then checked with RTL compilers and lint tools.
Automatic test bench generation using the same interface specification as the module under test and the	Test benches are updated based on the changing vector and module interface specifications.	Not available
Concise CSL language representations of design specifications	A high level specification language allows the designer to create complex designs using a fraction of the code that they would otherwise use and allows the design(s) to make changes rapidly.	Languages for specific solutions such as Vera® and E® for verification, System C® for high level design, HDL Designer® for design hierarchy and interconnect capture and visualization.
describe the architectural level components in a chip design using a concise syntax	Save time writing the code and generate correct component level C/C++and RTL code by construction.	In house code generation tools
Generate registers of different types (counter, interrupt,…) and optionally associate them with a memory map location	Eliminate design bugs when instantiating common elements.	Bluespec® / Bluesprint® / Memory map, interconnect ,and register creation using RDL®
Generate vectors used for testing using the same specification language as the interconnect specification files	Maintain consistency between interfaces of modules, test benches, and C/C++ simulators	Not available?
Generate C/C++ and RTL constants and address range checkers for memory maps	The C/C++ and RTL code design databases and the documentation are in sync at all stages of the project.	Bluesprint®
Generates connectivity and memory map, C++ and RTL code and documentation (pdf, doc, fm, HTML).	Avoid the creation and the maintenance of Makefiles or the dependency based build systems for the C/C++ and RTL front end code generation step	Different tools generate C++, RTL, and documentation. RDL®
Generate interfaces for C/C++ simulator vector generators	Interface consistency between the test bench instantiation of the module under test and the test vector memory in the test bench and the vector generator in the C/C++ simulator	Not available
Generate interfaces for modules	Interface consistency between modules	EDA and in house point tools. Do not integrate them with other tools.
Generate module interfaces for test benches, instantiate vector memories for test benches, and/or connectssocket PLI’s to test benches	Interface consistency between module under test and the test bench instantiation of the module under test	EDA and in house point tools. Do not integrate with other tools.
One specification language with support for many different types of chip components	No need to learn many different in house tool languages	Not available
Provide one API/database for all tools solutions	Check the interaction of all specification files in one database without having to use a code generator and an RTL compiler/simulation cycles	Not available
Rapid compilation times	Users can make architectural and design changes quickly	In house connectivity tools
RTL Compilation checks prior to high level language code generation	Errors in specification are found in the CSL compilation step and in the post code generation RTL compile step thus saving time. This is critical for large designs which can take (minutes to) hours to compile on a commercial RTL compiler/simulator/synthesis tool	Leda® checks for signal width consistency
Use a single point solution RTL like language instead of many languages	Lower learning curve for new engineers by using only one additional language for front end RTL design. Eliminate the cost of maintaining in house design automation tools	Not available
Verilog parser reads the existing designs into database	Existing designs are easily integrated with CSL specifications	In house applications.

Software Components
The list of CSLC software components is shown in the table below. Note that some components are still under development. The table lists the component and a description of the component in terms of the code that the component generates or the actions that the component performs or the way that the user interacts with the CSLC. The generated components are either C++ or RTL design or verification components or documentation.

Software component	Description	Availability
csl_warn_error	Warning and error module. Used by all software components. It provides a consistent way of reporting warnings and errors to users and developers	2007-Q1
csl_auto_router	Connects signals, signal groups, interfaces, ports, and instances in different scopes	2007-Q1
csl_const_expr_eval	Evaluates constant expressions in CSL and RTL	2007-Q1
csl_interconnect	Creates the design hierarchy and the interconnect	2007-Q1
csl_language	Language basics such as compile time constants and common constructs and methods that are shared between different CSL components	2007-Q1
csl_memory_map	Generates the RTL/C++ memory map for a chip.	2007-Q1
csl_testbench	Generates the RTL/C++ test bench components for a chip.	2007-Q1
csl_verification_components	Generate the C++/RTL vector writers and and readers	2007-Q1
csl_cdom_analysis	Analysis code that detects the correct and incorrect structures.	2007-Q2
csl_register	Generates the RTL /C++ different register types on a chip	2007-Q2
csl_register_file	Generates the RTL register files on a chip	2007-Q2
csl_fifo	Generates the RTL FIFO’s on a chip	2007-Q2
csl_pipeline	Generates the RTL pipelines on a chip	2007-Q2
csl_code_generation	Generates RTL and C++ code	2007-Q2
csl_command_shell	The CSLC command shell which is used to control a CSLC session	2007-Q2
csl_csl_analysis	Analysis code that detects correct and incorrect structures.	2007-Q2
csl_pro_con_mag	Generates the producer - consumer memory address generators on a chip	2007-Q2
csl_pscqn	Generates the RTL performance, status, control, query network on a chip	2007-Q2
csl_bus_ifc	Generates the RTL SOC unit level bus interface unit on a chip	2007-Q4
csl_buses	Generates the RTL custom on chip buses on a chip	2007-Q4
csl_gui	Graphical user interface for the tool. It contains a menu, a command shell, graphical views of the design and spreadsheet for entering information.	2007-Q4
csl_chip_contoller	Generates the chip controller logic.	2007-Q4
csl_clock_sync	Generates the RTL clock synchronizers on a chip	2007-Q4
csl_clock_tree	Generates the RTL/C++ clock tree on a chip	2007-Q4
csl_csim	Generates the C++ behavioral simulator	2007-Q4
csl_isa	Generates the custom instruction set and RISC like processor on a chip	2007-Q4
csl_regress	Generates the regression environment for a chip design	2007-Q4
csl_switch	Generates different types of switches	2007-Q4
csl_fpga	Generates the pin files to connect the FPGA’s to the PCB. Can be used to build FPGA models for accelerated HW simulation.	2007-Q2
csl_math_units	Generates the math units on chip including filters and adder trees. Uses fixed point arithmetic	2008-Q2
csl_memory_controller	Generates the RTL/C++ memory controller on a chip	2008-Q2
csl_mbist	Generates the RTL/C++ MBIST code for the SRAM’s on a chip	2008-Q2
csl_schematic	The CSLC schematic generator creates the interconnect between the RTL modules on different ASIC’s and FPGA’s and connects them through the pads, and PCB’s	2008-Q4
csl_asm	Generates the application specific SRAM’s on a chip	2009-Q4
csl_memory_compiler	Generates the SRAM’s on a chip	2009-Q4
csl_rtl_floorplaner	The CSLC floor planner ties the chip interconnect specification to the block placement and connectivity on the die.	2009-Q4
csl_soc_bus	Generates the RTL system on chip components	2009-Q4

CSL Language Classes
The table below shows a list of CSL classes that are used to create the design and verification specification. Some classes use sub classes to build the design and verification environment. The class methods are not shown. The design and verification components that are generated by the CSLC are shown in the table. Each component is broken down by its constituent parts.

CSL Category	CSL Component	Description	Availability
csl_interconnect	csl_interface	An interface of a unit which contains ports.	2006-Q4
csl_interconnect	csl_port;	A port in a unit interface	2006-Q4
csl_interconnect	csl_signal	Creates the connections between modules in the design hierarchy. Signals need not to be specified between two end points. An auto router will automatically connect two or more end points. It allows design teams to rapidly change hierarchies.	2006-Q4
csl_interconnect	csl_signal_group	Group signals together to create a named composite signal.	2006-Q4
csl_interconnect	csl_unit	A functional design unit (i.e. Verilog equivalent is a module and in C++ a class) which is used to create the design hierarchy.	2006-Q4
csl_language	compile time vars	if, if else, and for are supported	2006-Q4
csl_language	csl expressions	Basic Boolean and arithmetic expressions. Constant expressions are evaluated	2006-Q4
csl_language	csl_bitrange	Bit range object (example [31:0]) Bit ranges can be defined recursively. / Bit ranges can be used to build other bit ranges.	2006-Q4
csl_language	csl_cell	A bit range object that can have enumerated types assigned to it. Cells can be defined recursively. Cells can be used to build bit ranges.	2006-Q4
csl_language	csl_list	A list container for holding elements of the same type. Operations can be performed on all elements of a CSL list object.	2006-Q4
csl_memory_map	csl_memory_map	The CSLC tool can generate the memory map for a chip design from a CSL memory map specification. The CSLC will generate the C/C++ and RTL constants which represent the memory addresses of specific elements in the design as well as address range checkers and decoders.	2006-Q4
csl_register	csl_register	Generate the C/C++ and RTL register implementations for a chip design from a CSL register specification. Registers can be associated with addresses from the CSL memory map specification. Different types of registers (counter, interrupt, ...) can be generated. Registers can be connected to signals using the CSLC interconnect specification.	2006-Q4
csl_register_file	csl_register_file	The CSLC tool will generate the C/C++ and RTL register file implementations for a chip design from a CSL register file specification. Register files can be associated with addresses from the CSLC memory map specification, thus avoiding coding errors. Different register file personalities can be generated which avoids common coding errors by designers.	2006-Q4
csl_test bench	csl_event	A clock or boolean equation which represents a repetitive event in time.	2006-Q4
csl_test bench	csl_test bench	The CSLC tool will automatically generate test benches for each module in the design. The design under test can be driven with test vectors which either	2006-Q4
csl_vector	csl_teststate	The architectural test state specification associates a single aggregate state element (register file, FIFO, SRAM,…) specified in the CSL specification and associates the state element with a architectural test state name, the event used to capture the state, clock domain, reset signal, max number of frames (snap shots of the state element at various times. Vectors are generated by C/C++ simulators. Vectors are used for verification purposes by test benches.	2006-Q4
csl_vector	csl_vector	A vector specification which groups signals together specified in the CSL interconnect specification and associates the signals with a vector name, clock domain, reset signal, the event used to capture the vectors, and the max number of vectors,… Vectors are generated by C/C++ simulators. Vectors are used for verification purposes by test benches. Maintain consistency between interfaces of modules, test benches, and C/C++ simulators. The output test vectors are compared to the output of the design under test.	2006-Q4
csl_bus	csl_bus	Custom bus generator based on industry standard flow control concepts. Flow control is done using handshaking or valid/stall logic.	2007-Q2
csl_bus	csl_packet	Define packet formats. CSLC automatically generates the data framers and deframers.	2007-Q2
csl_bus	csl_payload	Define payloads for packets. CSLC automatically generates the data framers and deframers.	2007-Q2
csl_csim	csl_csim	C++ simulator code	2007-Q2
csl_fifo	csl_fifo	Generates the C/C++ and RTL FIFO implementations for a chip design from a CSL FIFO specification. FIFO’s can be associated with addresses from the CSLC memory map specification and different FIFO personalities can be generated which avoids common coding errors by designers. Optional performance counters can be added to discrete FIFO’s.	2007-Q2
csl_mbist	csl_mbist	MBIST	2007-Q2
csl_pipeline	csl_pipeline	Generates the C/C++ and RTL pipeline implementations for a chip design from a CSL pipeline specification. Complex pipelined and parallel pipelined registers can be connected to signals with pipe stage suffixes using the CSLC interconnect specification in conjunction with the CSL pipeline specification. Pipe stages are checked for correct connections and pipelines are checked for correct latencies using the CSLC analysis engine.	2007-Q2
csl_pro_con_mag	csl_pro_con_mag	producer consumer memory address generators on a chip	2007-Q2
csl_pscqn	csl_pscqn	Performance, status, query, control, network. An out of band network that is used to measure, monitor, configure, and control the chip design.	2007-Q2
csl_register	csl_table	A table is a two dimensional register that has named fields. Examples of tables are multimedia memories which are partitioned into hierarchies for the purposes of encoding and decoding different multimedia standards	2007-Q2
csl_regress	csl_regress	Regression environment an script generator for a chip design project	2007-Q2
csl_bus_ifc	csl_bus_ifc	Hardware abstraction layer interface unit between custom logic modules and standard on chip SOC buses.	2007-Q4
csl_chip_contoller	csl_chip_contoller	A unit which controls the operation of the pscqn, the explicit control of clock domains (on/off), the clock configuration, the memory controller operation, the chip operating mode (normal/diagnostic/test/power on self test), and the custom test logic on the chip (memory address write/read test, unit self test, SRAM MBIST, I/O loopback, external bus loop back self test, internal bus loop back self test, ). Controlled via a simple RISC like instruction set which is loaded via JTAG, a port on the chip, or a memory write.	2007-Q4
csl_clock	csl_clock	Define a clock which is used in design and verification components.	2007-Q4
csl_clock	csl_clock_gate	Gated clock	2007-Q4
csl_clock	csl_clock_mux	Clock multiplexer	2007-Q4
csl_clock	csl_clock_switch	Clock switch	2007-Q4
csl_clock_sync	csl_clock_sync	Clock synchronizers on a chip	2007-Q4
csl_fpga	csl_fpga	FPGA configuration files	2007-Q4
csl_isa	csl_isa	Instructions set architecture	2007-Q4
csl_isa	csl_isa	Instruction set architecture code generator. Creates instruction decoders / Create basic RISC pipelines and Micro assembler.	2007-Q4
csl_switch	csl_clos_switch	CLOS switch	2007-Q4
csl_switch	csl_pt_to_pt_switch	Opint to point switch	2007-Q4
csl_switch	csl_sen_switch	Shuffle exchange switch	2007-Q4
csl_switch	csl_xbar_switch	Cross bar switch	2007-Q4
csl_math_units	csl_math_adder_tree	Adder tree	2008-Q2
csl_math_units	csl_math_filter	Filter	2008-Q2
csl_rtl_floorplaner	csl_rtl_floorplaner	Floor planner ties the chip interconnect specification to the block placement and connectivity on the die.	2008-Q4
csl_schematic	csl_schematic	Creates the interconnect between the RTL modules on different ASIC’s and FPGA’s and connects them through the pads, and PCB’s	2008-Q4
csl_soc_bus	csl_soc_bus	RTL system on chip bus (OCP, Amba)	2008-Q4
csl_asm	csl_asm	Application specific memory	2009-Q4
csl_memory_controller	csl_memory_controller	Memory controller	2009-Q4
csl_sram	csl_sram	Memory compiler	2009-Q4