Automatic design hierarchy and interconnect generation

Fastpath Logic's chip specification language (CSL) compiler automates generation of the design hierarchy and the interconnect in C++ simulator, RTL testbench and RTL design code.

Capturing the design hierarchy and interconnect specification in a language other than RTL is more efficient for the following reasons:

- The specification is separated from the implementation.
- Both C++ and RTL code is generated.
- The design hierarchy and interconnect are verified by the interconnect checker.
- An interconnect report is generated which details the connection to each bit in the hierarchy.
- The interconnect specification is sparse since connections between end points eliminate the intermediate formal to actual signals.
- Intermediate formal to actual signals are automatically generated.
- Other components such as testbenches and verification vectors need to “know” about the module interfaces and any changes to the module interfaces.
- Proliferation projects can reuse the design hierarchy and interconnect specification.
- Changes to the design hierarchy above the leaf level do not “break” connections.
- Different design hierarchies can be explored in conjunction with a floor planning tool to find any potential problems with the chip's floor plan and routing between modules. Longest paths can also be discovered.
- Interface “contracts” between RTL designers, between C++ simulator unit owners, and between C++ simulator writers, testbench writers, and RTL designers can be enforced from a central point since the C++ and RTL interfaces are automatically generated.

Generates RTL and C++ design hierarchy and instances (interconnect) code.
Interconnect specification can be easily modified at the end points (more on that later).
Unit interface and connectivity documentation is automatically produced.
C++ unit interfaces can be automatically connected to automatically generated vector generators to create vector files for verification of the DUT.
RTL units can be automatically instantiated in automatically generated testbenches.

The design hierarchy is created using a container class called a csl_unit. Connectivity objects are instantiated in the csl_unit. Connectivity objects include the following:

Interconnect types
The following types are used to build chip interconnects and design hierarchies
- Enumerated types
- Bit ranges
- Fields
- Signals
- Signal groups
- Ports
- Interfaces
- Units
Enum types are declared only in the global scope. An enum is a collection of named integer constants, called enum items. Enum items can have a value assigned.
Bitranges are objects in CSL and can have an upper and lower index or a width.
Bitranges can be added to the following CSL connectivity objects: field, signal, and port. Bit ranges are a variable in CSL.
Fields are inherited from bit range. Fields can have an associated name. Fields can have an associated enum or enum item. Fields are an object in CSL. Fields can be non-hierarchical or hierarchical.
Units contains an interface and unit instances.
Auto Connect statements
Connectivity objects include signals which connect the unit instances to each other, formal to actual name mappings in the unit instantiations (name changes, constant assignments, concatenations, expressions, and part selects).
Signal groups: Group signals and other signal groups together into aggregate structures.
Interfaces: group ports and other interfaces together into aggregate structures.

Auto router
The cslc auto router automatically connects endpoints in different modules. Intermediate connections, formal to actuals, are automatically created. Changes in the design hierarchy do not affect connect statements.
The following example shows a design hierarchy. The two end points are connected via a CSL connect statement.
The intermediate formal to actual mappings are added to the module instances in the C++ simulator and RTL design code. The connection between the two end points is show in figure 2.
Figure 1.Connection end points
Interconnect documentation is generated for each module interface and for each instance.
Figure 2.Connection between endpoints

Fastpath Logic, Inc.
PO Box 188
Palo Alto, CA, 94302-0188
Phone 650-331-0702
email info@fastpathlogic.com
web www.fastpathlogic.com