# Introduction
CSL Memory Map is used to associate memory addresses with state element objects which name specified in CSL or with symbolic names.
# Description
The CSL memory map specification is used to describe map of the memory.
Because a memory map is very important for the big projects and not only, CSL language permits user to creates its map of the memory.
Designers on chip design projects specify memory maps which are used by the following groups within the chip design team:
- RTL team;
- C++ chip simulator team;
- test team;
- software driver team.
Members of each team must have the correct address specification implemented in their code at all times. Using one source to generate the RTL and C++ constants and functions associated with the memory map ensures that all team members are using the same address constants at all times.

# Features
With CSL Memory Map the user can create three memory map types:
flat, as a normal memory map,
- virtual, with global address and local address (can include one ore more flat maps at the address specified as base address),
- hierarchical, for different units.
There are two modes for calculate global address for the virtual memory map.
The hierarchical memory maps are automatically structured, the user can call very easy any unit.
The virtual map will auto calculate the global address (based on the base address or by shifting the address)
By declaring a memory map as global if there are many users (developers) and each one has a local memory map, they can add their local memory map to the global memory map without any conflict.
# Architecture Diagram

CSL memory map specification file
cslc
C++
code
Verilog
code
specs

# Benefits
Application code which refers to variable names is much clearer and much less sensitive to changes than code containing hard-coded numbers.
With the CSL Memory Map the user can:
- create one or more different memory maps for the same memory structure,
- include one or more memory maps into another memory map,
- define different access rights, or invalid ranges of addresses.
- generate Verilog code, C++ code, and specifications (pdf or doc).
The user can create memory maps much easier and much structured way.
The virtual memory map has two modes for calculate global address:
- with base address
- with page number in address
CSL Memory Map supports auto increment; the address is automatically incremented and the current element is added to the current address. The reserved address ranges are skipped.
# Dependencies
Any kind of memory element can be mapped into a memory map. The following memory elements must be available in order to be mapped: registers, register files, separate flip-flops, FIFOs, SRAMs.
# Supported formats
The memory map supports the following input/output formats.
## Input:
CSL, Verilog, VHDL
## Output Generators Provided:
CSL, Verilog, VHDL, C/C++, HTML, PDF

To find out how CSL Memory Map can make your chip design more efficient; contact Fastpathlogic Sales today.

# Introduction
CSL Memory Map is a design tool that increase team productivity when facing complexity related to design phases that require mapping to system memory of hardware components developed by different internal or external groups.
Using the CSL Memory Map tool the user can easily map different memory elements available in design modules and create a unified map of the entire design. Application code which refers to variable names is much clearer and much less sensitive to changes than code containing hard-coded numbers.
# Description
Memory maps are important parts of all actual complex designs. Their use is multi fold and spread over the entire cycle of a SoC design. Different aspects of design that make use of memory maps include:
- development of system architecture;
- logic design;
- software development;
- design validation by verification and test;
- generation of documentation.
During the design process several groups within a SoC design team have to specify, use and modify the memory maps: system architecture team, RTL team, software team and test team.
Every design refinement or iteration implies modification of design specification which usually also affects in some degree the initial memory map specification.
The use of CSL Memory Map guaranties that the members of all teams have the correct address specification implemented in their code at all times.
CSL Memory Map provides one source to generate all needed outputs including RTL and C++ constants (defines or header files), functions that manipulate associated memory map objects (optional) and documentation in different formats like text, HTML or PDF.
CSL Memory Map is based on the same language concepts and uses the same syntax as all tools in the CSL package.
# Concepts
In the specification of the design memory map the designer can use different CSL objects like fields, registers, memory map pages, memory map.
Different memory map types can be used in order to address various levels of complexity.
Flat memory maps are
In more complex designs that imply several processing modules, each one having its own memory units, the designer can reduce complexity by one order of magnitude by using hierarchical memory maps.
Using CSL Memory Map designers can also make specifications for systems that use virtual memory mechanisms. Virtual pages can be specified using page number and address or with base address.
Specification of hierarchical memory maps can be done using top -down or bottom up methodologies.
In the top-down methodology the designer starts from the general overview of the SoC memory and after that continues with the description refinement by specifying smaller memory blocks that need to be mapped into the memory space.
The bottom-up methodology starts by defining smaller memory map blocks which are then assembled in bigger memory maps until all memory elements are mapped into the memory space.
Specification of memory map objects within the memory address space can be done in two ways allowing a big amount of flexibility through intuitive set of commands. By using commands like set_lower_address or set_upper_address the absolute addresses for the position of a memory element is specified.
Relative position can be specified using commands like next, previous, first, last and explicit or implicit increment mechanisms.
# Use of Memory Map
## Development of system architecture
Developing system architecture implies partitioning the design in subsystems that can be implemented either by hardware or software. Functionality of system components and interrelationship between the two worlds can not be imagined without using memory elements that need to be mapped into the system memory address space.
## Logic design
During logic design memory maps are involved in the specification of hardware elements associated to memory maps (flip-flops, registers, memory cells, register files, FIFOs). Memory maps define the specification of interconnection between memory map elements and other design modules are used to generate the access and control logic for memory map elements. Based on interconnect and memory map specification, the compiler generates address, data and control lines (set, reset, enable), clock lines and even access protocols.
Consistency that must be preserved between different stages of logic design is assured by CSL Memory Map specification.
## Software development
Complex system systems that include large number of functional and configuration registers must have user friendly ways to access registers, variable length fields and individual register flags.
CSL Memory Map can generate necessary header files to be used by software team in order to develop device drivers or by users to build specific applications.
## Design validation by verification and test
Verification and test are important parts of the designing process and take a big part of the time allocated to system development.
CSL Memory Map offers an important help in developing tests benches and verification set-ups . The two operations can be speed up by taking advantage of the hierarchical structure of the CSL Memory Map. Design can be tested at different hierarchical levels resulting in the increasing of fault detection speed and a better localization of defective modules.
## Documentation generation
Different design groups have different perspectives on the design modules and their mapping to the system memory. A good correlation between the groups is not possible without a good documentation of all modules.
CSL Memory Map can generate documentation for all perspectives an in all different formats that are standard today.
# Benefits
With the CSL memory map the designer can create one or more different memory views for the same memory structure.
include one or more memory maps into another memory map creating a hierarchy that can mirror the design hierarchy,
Defining different access rights, visibility, or invalid ranges for memory addresses, the compiler can generate memory map output files for specific users (hardware team, software team, end users).
Memory map specification can generate outputs in different format like design files containing Verilog code or C++ code, and documentation files in formats like pdf, html or doc.
# Dependencies
Any kind of memory element available in CSL language can be mapped into a memory map. The following memory elements must be available in the design library in order to be mapped: registers, register files, separate flip-flops, FIFOs, SRAMs.
# Supported formats
The memory map supports as input formats CSL and HDL ( Verilog, VHDL) and as output formats CSL, Verilog, VHDL, C/C++, HTML, PDF.

# Introduction
CSL Memory Map is used to associate memory addresses with state element objects which name specified in CSL or with symbolic names.
# Description
The CSL memory map specification is used to describe map of the memory.
Because a memory map is very important for the big projects and not only, CSL language permits user to creates its map of the memory.
Designers on chip design projects specify memory maps which are used by the following groups within the chip design team:
- RTL team;
- C++ chip simulator team;
- test team;
- software driver team.
Members of each team must have the correct address specification implemented in their code at all times. Using one source to generate the RTL and C++ constants and functions associated with the memory map ensures that all team members are using the same address constants at all times.

# Features
With CSL Memory Map the user can create three memory map types:
flat, as a normal memory map,
- virtual, with global address and local address (can include one ore more flat maps at the address specified as base address),
- hierarchical, for different units.
There are two modes for calculate global address for the virtual memory map.
The hierarchical memory maps are automatically structured, the user can call very easy any unit.
The virtual map will auto calculate the global address (based on the base address or by shifting the address)
By declaring a memory map as global if there are many users (developers) and each one has a local memory map, they can add their local memory map to the global memory map without any conflict.
# Architecture Diagram

CSL memory map specification file
cslc
C++
code
Verilog
code
specs

# Benefits
Application code which refers to variable names is much clearer and much less sensitive to changes than code containing hard-coded numbers.
With the CSL Memory Map the user can:
- create one or more different memory maps for the same memory structure,
- include one or more memory maps into another memory map,
- define different access rights, or invalid ranges of addresses.
- generate Verilog code, C++ code, and specifications (pdf or doc).
The user can create memory maps much easier and much structured way.
The virtual memory map has two modes for calculate global address:
- with base address
- with page number in address
CSL Memory Map supports auto increment; the address is automatically incremented and the current element is added to the current address. The reserved address ranges are skipped.
# Dependencies
Any kind of memory element can be mapped into a memory map. The following memory elements must be available in order to be mapped: registers, register files, separate flip-flops, FIFOs, SRAMs.
# Supported formats
The memory map supports the following input/output formats.
## Input:
CSL, Verilog, VHDL
## Output Generators Provided:
CSL, Verilog, VHDL, C/C++, HTML, PDF

To find out how CSL Memory Map can make your chip design more efficient; contact Fastpathlogic Sales today.

# Introduction
CSL Memory Map is a design tool that increase team productivity when facing complexity related to design phases that require mapping to system memory of hardware components developed by different internal or external groups.
Using the CSL Memory Map tool the user can easily map different memory elements available in design modules and create a unified map of the entire design. Application code which refers to variable names is much clearer and much less sensitive to changes than code containing hard-coded numbers.
# Description
Memory maps are important parts of all actual complex designs. Their use is multi fold and spread over the entire cycle of a SoC design. Different aspects of design that make use of memory maps include:
- development of system architecture;
- logic design;
- software development;
- design validation by verification and test;
- generation of documentation.
During the design process several groups within a SoC design team have to specify, use and modify the memory maps: system architecture team, RTL team, software team and test team.
Every design refinement or iteration implies modification of design specification which usually also affects in some degree the initial memory map specification.
The use of CSL Memory Map guaranties that the members of all teams have the correct address specification implemented in their code at all times.
CSL Memory Map provides one source to generate all needed outputs including RTL and C++ constants (defines or header files), functions that manipulate associated memory map objects (optional) and documentation in different formats like text, HTML or PDF.
CSL Memory Map is based on the same language concepts and uses the same syntax as all tools in the CSL package.
# Concepts
In the specification of the design memory map the designer can use different CSL objects like fields, registers, memory map pages, memory map.
Different memory map types can be used in order to address various levels of complexity.
Flat memory maps are
In more complex designs that imply several processing modules, each one having its own memory units, the designer can reduce complexity by one order of magnitude by using hierarchical memory maps.
Using CSL Memory Map designers can also make specifications for systems that use virtual memory mechanisms. Virtual pages can be specified using page number and address or with base address.
Specification of hierarchical memory maps can be done using top -down or bottom up methodologies.
In the top-down methodology the designer starts from the general overview of the SoC memory and after that continues with the description refinement by specifying smaller memory blocks that need to be mapped into the memory space.
The bottom-up methodology starts by defining smaller memory map blocks which are then assembled in bigger memory maps until all memory elements are mapped into the memory space.
Specification of memory map objects within the memory address space can be done in two ways allowing a big amount of flexibility through intuitive set of commands. By using commands like set_lower_address or set_upper_address the absolute addresses for the position of a memory element is specified.
Relative position can be specified using commands like next, previous, first, last and explicit or implicit increment mechanisms.
# Use of Memory Map
## Development of system architecture
Developing system architecture implies partitioning the design in subsystems that can be implemented either by hardware or software. Functionality of system components and interrelationship between the two worlds can not be imagined without using memory elements that need to be mapped into the system memory address space.
## Logic design
During logic design memory maps are involved in the specification of hardware elements associated to memory maps (flip-flops, registers, memory cells, register files, FIFOs). Memory maps define the specification of interconnection between memory map elements and other design modules are used to generate the access and control logic for memory map elements. Based on interconnect and memory map specification, the compiler generates address, data and control lines (set, reset, enable), clock lines and even access protocols.
Consistency that must be preserved between different stages of logic design is assured by CSL Memory Map specification.
## Software development
Complex system systems that include large number of functional and configuration registers must have user friendly ways to access registers, variable length fields and individual register flags.
CSL Memory Map can generate necessary header files to be used by software team in order to develop device drivers or by users to build specific applications.
## Design validation by verification and test
Verification and test are important parts of the designing process and take a big part of the time allocated to system development.
CSL Memory Map offers an important help in developing tests benches and verification set-ups . The two operations can be speed up by taking advantage of the hierarchical structure of the CSL Memory Map. Design can be tested at different hierarchical levels resulting in the increasing of fault detection speed and a better localization of defective modules.
## Documentation generation
Different design groups have different perspectives on the design modules and their mapping to the system memory. A good correlation between the groups is not possible without a good documentation of all modules.
CSL Memory Map can generate documentation for all perspectives an in all different formats that are standard today.
# Benefits
With the CSL memory map the designer can create one or more different memory views for the same memory structure.
include one or more memory maps into another memory map creating a hierarchy that can mirror the design hierarchy,
Defining different access rights, visibility, or invalid ranges for memory addresses, the compiler can generate memory map output files for specific users (hardware team, software team, end users).
Memory map specification can generate outputs in different format like design files containing Verilog code or C++ code, and documentation files in formats like pdf, html or doc.
UART / DMA / I2C / Memory / map / GPI0 / Eth / MAC / IM / DM / ALU / RF / SR / SEQ / Memory Bank0 / P0 / IM / DM / Pn / . . . / Memory Bank m / . . .
Figure 3. Mapping memory elements from the SoC.

# Dependencies
Any kind of memory element available in CSL language can be mapped into a memory map. The following memory elements must be available in the design library in order to be mapped: registers, register files, separate flip-flops, FIFOs, SRAMs.
# Supported formats
The memory map supports as input formats CSL and HDL ( Verilog, VHDL) and as output formats CSL, Verilog, VHDL, C/C++, HTML, PDF.

Memory Map Features	Benefits
Different kind of memory types: flat, hierarchical	Create one or more different memory maps for same memory structure in much structured way
Global address assignment for memory elements	Two ways to calculate global address for memory maps and automatically calculate the global address for hierarchical memory maps
Set access rights and permissions by group	Set the read/write permissions and the access right s for each group in the project from one central point. enables the project to control the access rights to individual memory elements for read or/ and write by hardware or/and by software
Reserved address ranges	Create reserved address ranges which cannot be assigned in the current design
Incremental design	Easy to modify the nitial memory map specification with minimal design effort
Illegal address ranges	Create illegal address ranges which cannot be assigned in the current design
Hierarchical memory maps	Create memory maps from unit address maps