# Introduction
CSL Register is used to define registers as memory elements. A designer can write a memory element specification for each new chip design.
# Description
Another category for CSL language is the CSL Register specification.
CSL Register specifications are compiled by the CSLC to create registers in the target language.
A register can be created using CSL Register syntax or by using CSL Field.
The memory element specification includes the following:
- name of the register,
- the width of the register,
- the field declarations,
- add registers to memory map
- attribute bits (read, write, shadow),
- control pins (set, clear, enable, write enable, etc).

Within registers fields can be named.
The fields are optional.
The user can assign an address for the register. See the CSL Memory Map data sheet for information assigning an address to a field, register.
The memory element specification is then checked for correctness.

Figure1. A register file that permits two read operations in the same time and one write operation
# Features
The CSL Register specification is used to create memory mapped state elements that are addressable by other hardware units or by software through writes or reads.
Using CSL Register the user can create different kind of registers like:
- counter registers,
- event registers,
- interrupt registers,
- linear feedback shift register (LFSR),
- status register,
- shift register,
  etc.

Registers can have synchronous or asynchronous control pins, clock pins, input and output pins.
The CSL registers optionally can support serial shift write and read pins.
A register can be connected to a signal or other connectivity object

The user can create registers with multiple writes or a multiple reads.
For a Counter Register the CSL language permits:
- to create counter with GRAY code output,
- to set the start value and the end count value,
- to set the count direction (incremental/
- decremental),
- to set a count direction using a control signal.
Register type	Description
Action Sequence	Action commands are loaded into a fifo. A go signal is sent and the commands are executed in sequence; when all commands are executed a done signal is asserted
Atomic Register	Hardware semaphore bit plus a data register
Counter Register	Up/down counter register
Control Register	Used to control other hardware elements
D-FF Register	Register with D flip-flops
Event Register	Captures events
Interrupt Register	Intrerrupt mask, interrupt enable, and interrupt registers
LFSR Register	Linear Feedback Shift Register- a shift register whose input bit is a linear function of its previous state
Shift Register	Register that shift the bits
Semaphore Register	Hardware semaphore register
Statistics Register	Capture statistics based on events
Status Register	records status

# Architecture Diagram

CSL register specification file
cslc
C++
code
Verilog
code
specs

# Benefits
With the CSL the user can easily create any kind of register and assign the register to a memory map location.
A read/write permission is specified for each field in the register. The address of the register is calculated either by incrementing the previous address or is explicitly specified using a number or a constant.
The user can create registers with discontinuous ranges.
With the CSL Register the user can generate different register types using same sintax.
CSL will generate Verilog code, C++ code and specifications for any register.

# Supported formats
## Input:
CSL, Verilog, VHDL
## Output Generators Provided:
CSL, Verilog, VHDL, C/C++, HTML, PDF

To find out how CSL Register can make your chip design more efficient; contact Fastpathlogic Sales today.

Register Features	Benefits
Different kind of register types	Enables to create one or more different registers like: counter, event, interrupt, LFSR, status, shift
Read and write permission	Enables to specify read/write permission for each field in the register or for entire registyer
Address ranges	Enables to create registers with discontinuous address ranges and automatically calculate the addresses
Multiple read and writes configurable	Enable to configure any register to permit one or many reads or writes
Register's output	Easy to create the negative output for any register, easy to configure a counter register to have output in Gray code
Almost same sintax for all kind of registers	Ability to configure characteristics for register much easier
Register's mask	Enables to create feedback mask for LFSR register and interrupt mask for interrupt register