CSL/CSLC
Infrastructure generation
for C++ cycle based simulation

---
C++ simulator features
Describe the architectural level components in a chip design using a concise syntax.
Concise CSL language representations of design specification is compiled and generates C++ cycle based simulator code.
Generates design hierarchy and connectivity code in C++ which is automatically connected to RTL testbenches.

---
C++ simulator features
Interconnect specification can be easily modified at the end points (more on that later).
Unit interface and connectivity documentation is automatically produced.
C++ unit interfaces can be automatically connected to automatically generated vector generators to create vector files for verification of the DUT.

---
Cycle based
simulation
concepts

---
Functional abstractions
A functionally equivalent simulator implements an abstraction that is functionally equivalent to the hardware implementation.
The abstraction executes faster than the hardware implementation.

---
Fan in cones
Circuit based fan in cones are combinational logic cones that implement boolean logic functions.
Even math functions can be reduced to boolean logic functions.
C++ cycle based simulators implement complex hardware functions using simplified , functionally equivalent logic.

---
Fan in cones (cont.)
Fan in cones in the cycle based simulator are implemented in C++ functions using functionally equivalent abstractions.

---
Register operations
Registers hold state.
The state is updated on the rising edge of clock and possibly an enable signal.

---
D to Q value propagation
Each register is associated with a particular clock. If the clock is active (and the optional enable is active) the value in the register's D variable is propagated to the register's Q variable on the rising edge of clock.

---
Multiple clock domains
Cycle based simulators can support multiple clock domains.
A clock module generates each of the clock signals.
The clock signals control the propagation of the D to Q values.

---
Simulation cycle

---
CSL_INSTANCE_TREE
Each design has an instance tree which is created by the architecture/design team.
The instance tree is constructed from the design hierarchy which describes the unit instances.
Connections are made between end points in the instance tree using connectivity objects.
The connectivity objects are typically located in the leaf level units.
The auto router adds the intermediate signals and ports to the unit instances with formal to actual connections which connect end points.

---
Cycle based
simulation
components

---
Register class
There are two variables in a register.
D-connected to the output of a fan in cone or the input of a unit and updated when the combinational logic is updated.
Q-(the state) updated when the clock signal and the optional enable signal are true. Connected to the input of a fan in cone, the output of a unit, or the D of another register.

---
Unit class
The unit class is used to instantiate other units, instantiate registers, and define execute functions (combinational logic).

---
Clock generator

---
Command shell

---
Simulator class

---
Vector writer class
Reads vectors from unit interfaces (ports) writes it out to a file or PLI socket (future)

---
Architectural writer class
Reads architectural state and writes it out to a file or PLI socket (future).

---
Ports
Input ports are connected to ports or signals using a static pointer.

---
Connections
Connection statements are created by the cslc to connect different units.
Connection statements also connect unit ports to vector writer classes.
Connections between ports are made in the build functions.

---
Execute function
The generated unit class contains a virtual execute function.
The execute function is defined by the user.
The execute function contains logic and register write and register read function calls.

---
Cslc generated C++
simulator features
Generate design hierarchies and module interfaces automatically.
Use C++ as the input language to specify the following:
design hierarchy
interconnect
connections to vector writers
constants
2D memory structures (register files)

---
Infrastructure component interfaces
The interfaces between C++ and C++ infrastructure components are automatically generated.
The interfaces between RTL and RTL infrastructure components are automatically generated.
The interfaces between C++ and RTL infrastructure components are automatically generated.

---
C++ simulator library components
Main simulation loop
Command shell
C++ simulator class libraries

---
Main simulation loop
The main simulation loop for a cycle based simulator performs the following operations:
Calculate the new outputs for each fanin cone and write the new values to the inputs of the registers (D).
For each clock that is active propagate the value from each register's D to Q.
Check if the command shell has any pending operations.
Repeat.

---
Command shell
The command shell is used to control the following operations in the cycle based simulator:
Number of simulation cycles to execute before stopping
Print out values
cd to units
ls units to inspect the signals and instances

---
C++ simulator class libraries
The C++ class libraries contain the following classes:
simulator execution loop
command shell
register
unit
vector writer
architectural state writer

---
Specifying the
cycle simulator

---
Simulator input specification
The CSL input specification is compiled by the cslc and generates both the C++ simulator infrastructure components and the RTL design and testbench components.

---
Compiling the
cycle based
simulator input
specification with
the CSL compiler

---
Compilation of C++ simulator
The C++ simulator is compiled with a Makefile.
The generated C++ simulator files are compiled into .o files and linked to the libcsim.a file.
The resulting binary is the C++ simulator executable.

---
Building the cycle
based simulator

---
Aggregate structures
Group signals together in aggregate structures-signal groups
Group ports together in aggregate structures-interfaces

---
Aggregate structures
Build hierarchies of groups (signal groups and interfaces) and scalars (ports and signals)

---
CSL interconnect types
The following types are used to build chip interconnects and design hierarchies
Enumerated types
Bit ranges
Fields
Signals
Signal groups
Ports
Interfaces
Units
Connect statements

---
Units
The csl_unit declares a design unit.
The csl_unit is defined in the global scope.
Unit instances and connectivity objects are added to units.
The csl_unit is the equivalent of a Verilog module.
The csl_unit is used to build design hierarchies.
The csl_unit is a class with a constructor.
CSL types are instantiated in the csl_unit.
The types, if applicable, may be modified in the csl_unit constructor.

---
Connections between units
Formal to actual name mappings
Expressions
Constants
Concatenations
Part selects
Aggregate structures

---
Design hierarchy rules
A tree of units
One root unit (top level unit)

---
CSL
Interconnect
Syntax

---
Bitranges
Bitranges are objects in CSL and can have an upper and lower index or a width.
Bitranges can be added to the following CSL connectivity objects:
Field
Signal
Port
(FUTURE) List using the set_bitrange command.
Bit ranges are a variable in CSL.

---
Bitranges
Declared with a width
csl_bitrange br_width(3);
Creates a bit range with a range of [2:0]
Declared with another bit range
csl_bitrange br_br(br_width);
The copy constructor copies the other bit range values to the new bit range.
Declared with a range
csl_bitrange br_range(5,3);
Creates a bit range from the numeric values.

---
Enumerated types
Enumerated types are used in interconnects to describe bus operations on buses and decoder output signal names.
Enum types are declared only in the global scope.
An enum is a collection of named integer constants, called enum items.
Enum items can have a value assigned.

---
Enumerated types
Examples:
csl_enum e_enum{
ADD,
SUB
};
csl_enum e{
a = 2,
b = 3,
c = 4 };

---
Fields
Fields are inherited from bit range.
Fields can have an associated name.
Fields can have an associated enum or enum item.
Fields are an object in CSL.
Fields can be non-hierarchical or hierarchical.

---
Field usage
Fields are used by signals and ports in the interconnect specification and by other CSL language constructs.
Decoders can be generated from signals which contain fields.
Fields can be added to ports and signals (more on that later).

---
Fields
Examples:
//non-hierarchical field
csl_field f1(3);
//hierarchical field
csl_field f2 {
f1 f1_0;
f2() {}
};

---
An enum can be associated with a field
Example:
csl_enum e_enum{
ADD,
SUB
};
csl_field fld(5,e_enum);
The enum e_enum is associated with the field named fld and the enum items associated to the field will be ADD = 00000 and SUB = 00001

---
Signals
The csl_signal type is used to create Verilog wire type connections.
csl_signal sig(5);
Creates a 5-bit signal with a bitrange of [4:0].
The default type is wire. Other types may be specified.
Signals are declared inside of units.

---
Signals
A csl_bitrange can be used to declare a csl_signal
csl_bitrange br0(5);
csl_signal s(br0);
Creates a signal with 5-bits.
csl_bitrange br1(5);
csl_signal r(br1 + br0);

---
Signal groups
Signals can be grouped together to form a single object which is more efficient to manipulate than performing the same operation on individual signals.
Signal groups are defined in the global scope.
Signal groups can contain other signal groups.

---
Signal groups
The csl_signal_group is used to gather related signals that connect from one point to another point in the design hierarchy.
csl_signal_groups may be combined with csl_signals and other csl_signal_groups.
csl_signal_group sg{
csl_signal a,b,c;
sg(){}
};
Creates signal group with three 1-bit signals.

---
Signal groups
The members of the csl_signal group are accessed using the C++ dot operator.
sg.a
sg.b
sg.c
accesses the individual members of the signal group.

---
Signal groups
Creates signal group sg1 with three 1 bit signals a,b,c.
Creates signal group sg2 with three 1 bit signals x,y,z and three 1-bit signals from
instance sg1.
Creates a signal group sg3 with
two 1 bit signals and six 1 bit
signals from sg1 and sg2_1.
csl_signal_group sg1{
csl_signal a,b,c;
sg1(){}
};
csl_signal_group sg2{
sg1 sg1;
csl_signal x,y,z;
sg2(){}
};
csl_signal_group sg3{
sg2 sg2_1;
csl_signal m,n;
sg3() {}
};

---
Signal groups
The members of the csl_signal group are accessed
using C++ notation.
sg3.sg2_1.x
sg3.sg2_1.y
sg3.sg2_1.z
accesses the individual members of the signal group instance sg2.

---
Signal groups
sg3.sg2_1.sg1.a
sg3.sg2_1.sg1.b
sg3.sg2_1.sg1.c
accesses the individual members of the signal group instance sg1.

---
Signal groups
Accessing the signals inside of the signal group:
csl_unit u{
sg3 sg3_1;
sg3 sg3_2;
u () {
sg3_1.sg2_1.sg1.a.set_type(wire);
sg3_1.sg2_1.z.set_type(reg);
sg3_2.m.set_type(wire);
sg3_2.n.set_type(reg); }
};

---
Ports
The csl_port is used to create ports for the csl_units (more later).
The csl_port are declared in a csl_unit.
The csl_port is instantiated the same way that csl_signals are instantiated except the port has a direction.
csl_port in(input,8);
csl_port out(output,8);

---
Interfaces
Interfaces are containers for the port list of a unit.
An interface is defined in the global scope.
Interfaces may be instantiated inside of other interfaces.
More than one interface of the same or different type may be added to one unit.
The interfaces may be instances of the same or different interfaces.

---
Interfaces
The generated interface Verilog code prefixes the name of the interface in front of the name of the port.

---
CSL interconnect code
Unit declaration
csl_unit u_ref {
csl_port in(input, 8);
csl_port out(output, 8);
u_ref () {}
};
csl_unit u_check {
csl_port x_in (input, 8);
csl_port x_out(output, 8);
csl_signal sgn_ref_data;
u_ref ref1(
.p_ref_in (x_in),
.p_ref_out(x_out));
u_check() {
sgn_ref_data.set_width(8);
}
};
Adding ports
constructor
Unit instantiation
formal to actual name mappings
CSL object settings

---
Including user logic in
C++ simulator units
The user overrides the generated class.
The virtual execute function is defined.
The units registers are declared in the private variable section of the class.
The units pipeline logic is placed in the exectute function.
class someUnit : public generatedUnit {
}
Parent Unit generated by cslc

---
C++ simulator
example

---
Interface and connection example
csl_interface ifc{
csl_port x(input),
csl_port y(input);
csl_port z(input);
ifc () {}
};
csl_unit unit{
ifc ifc_in,ifc_out;
unit(){
ifc_out.reverse();
}
};
u
ifc_out
x y z
x y z
ifc_in
u2
ifc_out
x y z
x y z
ifc_in
u
ifc_out
x y z
x y z
ifc_in
u1
ifc_out
x y z
x y z
ifc_in
u
ifc_out
x y z
x y z
ifc_in
u0
ifc_out
x y z
x y z
ifc_in

---
Interface and conection example (cont.)
csl_unit top{
unit u0, u1, u2;
top(){
u0.ifc_out.connect(
u1.ifc_in
);
u1.ifc_out.connect(
u2.ifc_in
);
u3.ifc_out.connect(
u0.ifc_in
);
}
};
u
ifc_out
x y z
x y z
ifc_in
u2
ifc_out
x y z
x y z
ifc_in
u
ifc_out
x y z
x y z
ifc_in
u1
ifc_out
x y z
x y z
ifc_in
u
ifc_out
x y z
x y z
ifc_in
u0
ifc_out
x y z
x y z
ifc_in