CSL/CSLC
Testbench Specification

---
Testbench
Concepts

---
Purpose
Testbenches are used to verify instances of designs under test (DUT).
A testbench is a structure designed to verify the functionality of an RTL design.

---
DUT's and vectors
DUT's can be tested at the leaf level, intermediate level, and/or top level of the RTL design.
Testbenches which instantiate units (DUTs) at any level in the chip design hierarchy can be automatically created.
Vectors can be extracted from any of the above levels in the simulation model.

---
Creating Vectors
Vectors can be created by a C++ simulator which models the behavior of the chip design.
Vectors can be written to a file or a socket.
The vectors are used to verify the chip design.

---
Vectors
Vectors are a set of values associated with an ordered set of ports.
Input vectors are called stimulus vectors.
Output vectors are called expected vectors.
C++ simulators generate vectors and RTL designs under test are verified using those vectors.

---
Creation
Testbenches are created by instantiating the design under test (DUT) and adding wrapper logic to apply stimulus to the DUT inputs and logic to check the DUT outputs, internal state, or state transitions.

---
Changes
Testbenches must change in response to changes in the DUT interface or internal logic.

---
C++ simulator vector writers
The vector port order is optionally specified in the CSL vector specification.
CSL vectors are compiled and generate the C++ simulator vector writers.
The C++ simulator unit ports are connected to the C++ simulator vector writer.

---
C++ simulator and vectors
When the C++ simulator executes, the vector writers capture the values of the ports at the unit interfaces, and creates stimulus and expected vector files or (future) writes the vectors to a socket or to DUT modules in the RTL testbench.
Vector memories in the RTL testbench are loaded by vector readers from files or (future) from a socket for co-simulation with an RTL testbench using PLI's.

---
Simulator vectors
The simulation model produces the vectors.
A testbench is used to apply the vectors and test the implementation DUT RTL.

---
Stimulus vector memory
The stimulus vector memory is loaded with a stimulus vector memory file.
The stimulus vector memory is connected to the input of the DUT.

---
Expected vector memory
The expected vector memory is loaded with a expected vector memory file.
The expected vector memory is connected to the expected vector comparator.

---
Testbench tool features
Automatically instantiates:
design under test (DUT) modules in the RTL testbench
vector memories in the RTL testbench
comparators in the RTL testbench

---
Testbench tool features
Automatically connects:
testbench memories to the DUT
testbench comparators to the DUT
FUTURE: socket PLI’s to the testbench

---
Current design and testbench integration problems
Currently the design and testbench implementations are built in separate processes.
Some testbenches may be built using specialized testbench languages such as Vera or Specman.
Users are unable to trace the design signals and the specialized testbench in the same waveforms.

---
Simulator, testbench, and RTL design integration
Testbenches are automatically connected to the generated C++ simulator and RTL design with a minimal amount of code (10-20 lines).
No port mappings are necessary.
Changes to the interfaces in the design propagate automatically to the testbench and simulator.

---
Simulator, testbench, and RTL design integration
The testbench and design RTL code will be consistent and no additional work will be required to integrate them.

---
Simulator, testbench, and RTL design integration
The RTL testbench will will look for vector files in the path specified in the CSL code.
The vector files are generated by the C++ simulator and are written to a directory.
Example: the testbench points to “in.vec”.

---
Simulator, testbench, and RTL design integration
Since each test generates a vector file an environment variable must be set by the user to point to the vector file directory.
Alternatively the user can run a script to set soft links to vector files.
Based on experience the former is preferred for many reasons.

---
Expected vector memory
The expected vector memory is loaded with a expected vector memory file.
The expected vector memory is connected to the expected vector comparator.

---
Alternative vector generation
Other vector sources include dedicated vector generators. The same principle applies. The vector writer is instantiated in the vector generator and files are created or sockets are connected to the testbench.

---
C++ simulator
The C++ Simulator is an equivalent model of the Verilog DUT at the chip, cluster and/or unit boundaries.

---
CSL
Testbench
Concepts

---
Automatically generate RTL testbenches
The CSL compiler (cslc) reads the CSL interconnect and testbench CSL code and generates the RTL testbench code.
The CSL testbench code specifies the CSL unit(s) to instantiate in the testbench.
The CSL units have associated CSL input and output vectors.

---
Generated C++ simulator, RTL testbench, and RTL interconnect/Unit interfaces
Generated components
compiler
Input file

---
Interface changes
CSL is designed to propagate interface changes in the DUT to the testbench with a minimal amount of intervention by the designer and verification engineer.

---
CSL vector
Stimulus and expected vectors must have a unit and a direction specified, using the CSL commands set_unit_name and set_direction.

---
CSL vector
Vectors are associated with a unit.
Vectors are used by the testbench, but are not instantiated in it.
The default checker type is cycle accurate.

---
CSL testbench
A testbench is declared in the global scope.
The design under test (DUT) in a testbench can be a unit, register, register file, memory or fifo.
A csl_testbench must have a clock signal set using the add_logic command with a specified period and time base.

---
C++ vector writer generation
The CSL input and output vector specification are used by the cslc to generate the C++ simulator vector writers.

---
C++ simulator
The C++ Simulator is an equivalent model of the Verilog DUT at the chip, cluster and/or unit boundaries.

---
Testbench code updates
Testbenches are updated based on the changing vector and DUT interface specifications.

---
Connection
The connection between C++ simulator and the testbench is made using verification components which are passed using PLI (socket based communication) or files (file based communication).

---
Random temporal testing
The Temporal interface Testbench uses stimulus and expect vectors from the C++ Simulator to drive the design under test.
The temporal interface Testbench “randomly“ asserts the control signals for the design under test to vary the relationships between the control signals.

---
Error counters
An error counter accumulates the total number of mismatches between the expected vectors and DUT output vector.

---
Match counters
A match counter accumulates the total number of matches between the expected vectors and DUT output vector.

---
State comparison
A testbench can compare the state from the C++ simulator with the state from the RTL design at each clock edge or transaction.

---
Architectural state
We define the architectural state of a unit as the state of all architecturally visible memory elements (flip-flops, registers, register files, FIFOs etc) in that unit.

---
State comparison example
An example of state comparison which is used would be the comparison of content of architecturally visible registers in C++ and RTL processor models. The testbench performs a comparison between the two sets of architectural states.

---
Generated files
CSLC testbench generates report files in order to describe the performance of the DUT.
Summary Reports: lists the number of vectors that passed and failed and whether the overall test passed.
DUT output vector file for debugging.

---
Post processing scripts
Scripts can be used to post process the output vectors or stales of C++ Simulator and RTL models.
Those scripts compare the outputs and generate a report.

---
CSL
Testbench
Code

---
First declare the units
csl_unit u_ref {
csl_port in(input, 8);
csl_port out(output, 8);
u_ref () {}
};
csl_unit u_check {
csl_port x_in (input, 8);
csl_port x_out(output, 8);
csl_signal sgn_ref_data;
csl_port clk(input);
u_ref ref1(
.in(x_in),.out(x_out));
u_check() {
sgn_ref_data.set_width(8);
clk.set_attr(clock);
}
};
Unit declaration
Add ports
constructor
Unit instantiation
formal to actual name mappings
CSL objects settings

---
Then associate vectors with a unit
csl_vector v_stim {
v_stim () {
set_unit_name(u_check);
set_direction(input); }
};
csl_vector v_exp {
v_exp () {
set_unit_name(u_check);
set_direction(output); }
};

---
Then create a testbench
csl_testbench tb {
csl_signal clk(reg);
u_check u_check(.clk(clk));
tb () {
clk.set_attr(clock);
add_logic(clock,clk,100,ps);
}
};

---
Generated Verilog code
module tb();
// Location of source csl unit: file name = line number = 33
  parameter SIM_TIMEOUT_CNT = 100;
 parameter V_STIM_MEM_WIDTH = 8;
  parameter V_STIM_ADDR_WIDTH = 0;
  parameter V_STIM_VECTOR_ID = 0;
  parameter V_STIM_VECTOR_VERSION = 0;
  parameter V_STIM_VECTOR_NAME = "v_stim";
  parameter V_STIM_VECTOR_FILE = "v_stim_output.vec";
  parameter V_STIM_VECTOR_RADIX = 0;
  parameter V_STIM_VECTOR_MAX_ERR = 0;
  parameter V_EXP_MEM_WIDTH = 8;
  parameter V_EXP_ADDR_WIDTH = 0;
  parameter V_EXP_VECTOR_ID = 0;
  parameter V_EXP_VECTOR_VERSION = 0;
  parameter V_EXP_VECTOR_NAME = "v_exp";
  parameter V_EXP_VECTOR_FILE = "v_exp_output.vec";
  parameter V_EXP_VECTOR_RADIX = 0;
  parameter V_EXP_VECTOR_MAX_ERR = 0;

---
Generated Verilog code (cont)
 reg clk; reg testbench_reset; reg rand_valid;
  integer file_mcd; integer report_file_mcd; integer cycle_cnt;
  reg [V_EXP_ADDR_WIDTH - 1:0] v_exp_u_check_match_count;
  reg [V_EXP_ADDR_WIDTH - 1:0] v_exp_u_check_mismatch_count;
  reg [V_EXP_ADDR_WIDTH - 1:0] v_exp_u_check_transaction_count;
  reg v_exp_u_check_mismatch;
  wire expect_out_valid; wire rd_en;
  wire version_err; wire id_err;
  wire stop_sim = cycle_cnt >= SIM_TIMEOUT_CNT;
  wire [7:0] u_check_in_x_in;
  wire [7:0] u_check_out_x_out;
  wire [7:0] u_check_out_x_out_expect;
  wire u_check_out_x_out_mismatch_en = u_check_out_x_out != u_check_out_x_out_expect;
  wire u_check_out_x_out_match_en = u_check_out_x_out == u_check_out_x_out_expect;
  assign rd_en = rand_valid;
  u_check u_check(.clk(clk), .x_in(u_check_in_x_in), .x_out(u_check_out_x_out));

---
Generated Verilog code (cont)
stim_expect_mem_template #(V_STIM_MEM_WIDTH, V_STIM_ADDR_WIDTH, V_STIM_VECTOR_ID,
        V_STIM_VECTOR_VERSION, V_STIM_VECTOR_NAME, V_STIM_VECTOR_FILE,
        V_STIM_VECTOR_RADIX)
        v_stim_u_check(.clock(clk), .id_err(id_err), .rd_en(rd_en), .reset_(testbench_reset),
        .valid(expect_out_valid), .vector_out(u_check_in_x_in), .version_err(version_err));
  stim_expect_mem_template #(V_EXP_MEM_WIDTH, V_EXP_ADDR_WIDTH, V_EXP_VECTOR_ID,
        V_EXP_VECTOR_VERSION, V_EXP_VECTOR_NAME, V_EXP_VECTOR_FILE,
        V_EXP_VECTOR_RADIX)
        v_exp_u_check(.clock(clk), .id_err(id_err), .rd_en(rd_en), .reset_(testbench_reset),
        .valid(expect_out_valid), .vector_out(u_check_out_x_out_expect), .version_err(version_err));
always @( posedge clk or negedge testbench_reset ) begin
    if ( ~testbench_reset ) begin
      cycle_cnt <= 0;
    end
    else begin
      cycle_cnt <= cycle_cnt + 1;
    end
  end

---
Generated Verilog code (cont)
initial begin
    $system("time stamp: +20%y %m %d");
    clk = 0; rand_valid = 1; testbench_reset = 1;
    #10 testbench_reset = 0; #20 testbench_reset = 1;
    file_mcd = $fopen("vectors.txt");
    if ( file_mcd == 0 ) begin
      $display("Error opening vectors.txt file");
      $finish;
    end
    $display(file_mcd, "Dut outputs vs expected vectors:\n");
    report_file_mcd = $fopen("report.txt");
    $dumpfile("wavesDefaultOutputFile_dump");
    $dumpvars(0, tb);
    $dumpon;
    v_exp_u_check_match_count = 0;
    v_exp_u_check_mismatch_count = 0;
    v_exp_u_check_transaction_count = 0;
  end

---
Generated Verilog code (cont)
always @( posedge clk ) begin
    $fdisplay(file_mcd, "dut name: %s", u_check, " expect vector name: %s", v_exp_u_check, "\n");
    $fdisplay(file_mcd, "dut output: %b", u_check_out_x_out, "expected output: %b", u_check_out_x_out_expect);
  end
  always @( posedge clk ) begin
    if ( stop_sim ) begin
      $fdisplay(report_file_mcd, "Status for expect vector %b", v_exp_u_check, "associated to dut %b", u_check, ":\n");
      $fdisplay(report_file_mcd, "Total number of comparisons: %b", v_exp_u_check_transaction_count, " out of which, passed: %b", v_exp_u_check_match_count, "\nOverall: %s", v_exp_u_check_mismatch_count?"failed":"passed");
    end
  end
  always #100 clk = ~clk;
always @( posedge clk or negedge testbench_reset ) begin
    if ( ~testbench_reset ) begin
      v_exp_u_check_mismatch_count = {V_EXP_ADDR_WIDTH,{1'b0}};
    end

---
Generated Verilog code (cont)
 else begin
      if ( u_check_out_x_out_mismatch_en ) begin
        v_exp_u_check_transaction_count = v_exp_u_check_transaction_count + 1'b1;
        v_exp_u_check_mismatch_count = v_exp_u_check_mismatch_count + 1'b1;
        $display("mismatch detected: dut %s shows value %b; evepect vector %s shows value %b\n ", "u_check", u_check_out_x_out, "v_exp_u_check", u_check_out_x_out_expect); end
      if ( v_exp_u_check_mismatch_count > V_EXP_VECTOR_MAX_ERR ) begin
        $display("Maximum number or errors allowed for vector %s has been reached", "v_exp_u_check");
      end end end
  always @( posedge clk or negedge testbench_reset ) begin
    if ( ~testbench_reset ) begin
      v_exp_u_check_match_count = {V_EXP_ADDR_WIDTH,{1'b0}}; end
    else begin
      if ( u_check_out_x_out_match_en ) begin
        v_exp_u_check_transaction_count = v_exp_u_check_transaction_count + 1'b1;
        v_exp_u_check_match_count = v_exp_u_check_match_count + 1'b1;
        $display("match detected: dut %s shows value %b; evepect vector %s shows value %b\n ", "u_check", u_check_out_x_out, "v_exp_u_check", u_check_out_x_out_expect);
      end end end
  endmodule

---
Creating a testbench using CSL
A testbench is declared in the global scope

---
Creating an RTL testbench using CSL
The DUT in a testbench can be a unit, register, register file, memory or FIFO

---
Creating a testbench using CSL
A csl_testbench must have a clock signal set using the add_logic command with a specified period and time base.

---
Creating a testbench using CSL
Then run cslc to generate the RTL testbench and the C++ simulator code.

---
RTL
Testbench
Code

---
RTL testbench
The RTL unit input interface is connected to a stimulus vector memory(s).
The RTL unit output interface is connected to a comparator which compares the DUT output and the expected vector from the expected vector memory.

---
RTL testbench
The testbench vector memory width is specified by the vector width.
The testbench vector memory stores the vector values.

---
RTL testbench
The stimulus vector memory contains the vectors that are used to drive the inputs of the DUT.
The stimulus vector memory is connected to the RTL DUT ports.

---
RTL testbench
The stimulus vector memory is read every cycle after reset is de-asserted in the testbench.
The stimulus vector memory is loaded with a stimulus vector memory file.

---
RTL Testbench
The expected vector comparator is connected to the expected vector memory and the DUT output vector.
The comparator checks that each valid DUT output vector is equal to the corresponding expected vector output memory.

---
Verification
Flow

---
Code generation and simulation flow chart

---
Using the generated code
Now run the C++ simulation and generate vectors which are written to files.

---
Using the generated code
Next run the RTL simulation and apply the stimulus vectors to the DUT and compare the results