CSL/CSLC
The Front End Chip Architecture, Design and Verification Productivity Solution

---
Part 3
CSLC Compiler

---
The CSLC

---
CSL Objects
Inter-
connect
Buses
Register
Bus
 interface
Producer
consumer
Register
file
CSLC ???
FIFO
Testbench
Verification
components
Pipeline
ISA
Memory
map

---
Tools (1) group tools under same headings as in slide 3

---
Tools (2)

---
Tools (3)

---
Tools (4)

---
Interconnect need this slide for each heading
Inter-
connect
Testbench
Buses
Register
Memory
map
Register
file
CSLC
Pipeline
ISA
Memory
controller
MBIST
Verification
components
FIFO

---
Interconnect need set of slides for each heading
Slide 10 and up need revision
Explain what CSLC interconnect does
CSL interconnect code specifies:
  - Design hierarchy
  - Interconnect objects:
    - units
    - ports
    - interfaces
    - signals
    - signal groups

---
Specification with interconnect. CSL code
Unit declaration
csl_unit u_ref {
csl_port p_ref_out(output, 8);
u_ref () {} };
csl_unit u_comp {
csl_port p_ref_in(input, 8), p_data_in(input,8);
csl_port p_valid(output);
u_comp () {} };
csl_unit u_check {
csl_port p_data(input,8);
csl_port p_valid(output);
csl_signal sgn_ref_data;
u_ref ref1(.p_ref_out(sgn_ref_data));
u_comp comp1(.p_ref_in(sgn_ref_data),.p_data_in(p_data), .p_valid(p_valid));
u_check() {
sgn_ref_data.set_width(8);
}
};
Adding ports
Instantiating units. Connection done by formal to actual mapping
CSL object settings

---
CSLC interconnect support
interconnect generation
generation of RTL and C++ files
building the interconnect

---
Verilog code do not need verilog
module u_ref(p_ref_out);
output [7:0] p_ref_out;
endmodule
module u_comp(p_ref_in,
p_data_in,
p_valid);
input [7:0] p_ref_in;
input [7:0] p_data_in;
output [0:0] p_valid;
endmodule
module u_check(p_data,
p_valid);
input [7:0] p_data;
output [0:0] p_valid;
wire [7:0] sgn_ref_data;
u_ref ref1(.p_ref_out(sgn_ref_data));
u_comp comp1(.p_data_in(p_data),
.p_ref_in(sgn_ref_data),
.p_valid(p_valid));
endmodule

---
Specification with interconnect
csl_unit u_ref {
csl_port p_ref_out(output,8);
u_ref () {} };
csl_unit u_comp {
csl_port p_ref_out(output,8),
p_ref_in(input,8),p_data_in(input,8);
csl_list l(p_ref_in,p_data_in);
csl_port p_valid(output);
u_comp() {} };
csl_unit u_check {
csl_port p_data(input,8),p_valid(output);
csl_signal sgn_ref_data;
u_ref ref0(.p_ref_out(sgn_ref_data));
u_comp comp0(.p_ref_in(sgn_ref_data),
.p_data_in(p_data),.p_valid(p_valid));
u_check(){
sgn_ref_data.set_width(8); } };
p_ref_in p_data_in
u_comp
p_valid
p_ref_out
u_ref
check
p_data
8
8
sgn_ref_data
p_ref_out
ref0
p_ref_in p_data_in
comp0
p_valid
p_valid

---
Interconnect tool features
FUTURE: Able to read pre-existing designs and CSL specifications into the same object model and check the combined designs.
Concise CSL language representations of design specifications.
Describe the architectural level components in a chip design using a concise syntax.
Generates connectivity, C++ and RTL code and documentation (PDF, DOC, HTML).

---
Interconnect tool features
Generate interfaces for modules interfaces for test benches, instantiate vector memories for test benches, and/or connects socket PLI’s to testbenches
Verilog parser reads the existing designs into database
Use a single point solution RTL like language instead of many languages.

---
Adding signal to multiple units
sgn_clk.set_attr(clock);
sgn_reset.set_attr(reset);
sgn_clk.connect(u_chip.u_chip0.sgn_clk);
sgn_reset.connect(u_chip.u_chip0.sgn_reset); }
};
csl_unit u_chip {
csl_signal sgn_clk(input);
csl_signal sgn_reset(input);
u_chip(){
u_chip
sgn_reset
sgn_clk
pc
im
id
rf
alu

---
Specification with interconnect
connectivity:
  - signals which connect the unit instances to each other
  - formal to actual name mappings in the unit instantiations

---
//declaring bitranges
csl_bitrange brd(8); // creates a bitrange [7:0];
csl_bitrange brs(2); // creates a bitrange [1:0];
//adding operand to interface
csl_interface opifc{
  - csl_port a(input,brd), b(input,brd);
  - opifc () {} };
//defining select signal interface
csl_interface selifc{
  - csl_port s(input,brs);
  - selifc () {} };
//defining output interface
csl_interface outifc{
  - csl_port o(output, brd);
  - outifc () {} };
Using bitranges
//defining arithmetic unit
csl_unit arith{
  - opifc opifc0;
  - selifc selifc0;
  - outifc outifc0;
  - arith(){
  - }
};
//defining logic unit
csl_unit logic{
  - opifc opifc0;
  - selifc selifc0;
  - outifc outifc0;
  - logic(){}
};

---
Bitranges
Bitranges can be added to the following objects:
Field
Signal
Register
Port
Instruction format
Instruction

---
An enum can be associated with a field
Example:
csl_enum e_enum{
ADD,
SUB
};
csl_field field(5,e_enum);

---
Using bitranges
opifc
outifc
8
8
u1
op
selifc
2
sel
opifc
outifc
8
u2
selifc

---
Specifying offset
csl_unit _2bit_flip_flop{
csl_port p_data(input),clk(input),enable(input),q(output);
_2bit_flip_flop() { p_data.set_width(2); } };
csl_unit ff_a {
csl_port p_data_a(input),clk_a(input),enable_a(input),q_a(output);
ff_a () { set_offset(2); } };
csl_unit ff_b { csl_port p_data_b(input),clk_b(input),enable_b(input),q_b(output);
ff_b () { set_offset(2); } };
csl_unit ff_c { csl_port p_data_c(input),clk_c(input),
enable_c(input),q_c(output);
ff_c() { set_offset(4); } };
csl_unit decoder {
csl_port dec_in(input,6), dec_out(output,64);
decoder () { add_logic(gen_decoder); } };
_2bit_flip_flop ff_[[a-c]](.p_data(in_[\1]),
.enable(enable), .clk(clk_[\1]),.q(out_[\1])));
csl_list(ff_[[a-c]].in_[\1]).connect(dcd.d_in);
enable
flip_flop_a
2
2
in_a
clk_a
out_a
[0:1]
flip_flop_b
6
2
2
64
decoder
in_b
[0:1]
[2:3]
clk_b
dec_in
out_b
[0:5]
flip_flop_c
2
2
in_c
clk_c
[4:5]
[0:1]
out_c

---
CSL_INTERFACE
Interfaces are containers for the port list of a unit
Instances of interfaces can be used in units that have same signal sets.
More than one interface of the same or different type may be added to one unit.
The interfaces may be instances of the same or different interfaces.

---
CSL_INTERFACE
Modifying the contents (adding, deleting or changing the port names) of the interface container modifies the contents of all instances of the interface.
The port directions of all signals in an instance of an interface may be reversed using the reverse() method
are not reversed signals connected to the port which have a dont_modify_direction attribute.

---
Interconnect tool features
FUTURE: Able to read pre-existing designs and CSL specifications into the same object model and check the combined designs.
Concise CSL language representations of design specifications.
Describe the architectural level components in a chip design using a concise syntax.
Generates connectivity, C++ and RTL code and documentation (PDF, DOC, HTML).

---
CSL_INTERFACE
Interfaces are containers for the port list of a unit
Instances of interfaces can be used in units that have same signal sets.
More than one interface of the same or different type may be added to one unit.
The interfaces may be instances of the same or different interfaces.

---
CSL_INTERFACE
Modifying the contents (adding, deleting or changing the port names) of the interface container modifies the contents of all instances of the interface.
The port directions of all signals in an instance of an interface may be reversed using the reverse() method
are not reversed signals connected to the port which have a dont_modify_direction attribute.

---
Interconnect tool features
FUTURE: Able to read pre-existing designs and CSL specifications into the same object model and check the combined designs.
Concise CSL language representations of design specifications.
Describe the architectural level components in a chip design using a concise syntax.
Generates connectivity, C++ and RTL code and documentation (PDF, DOC, HTML).

---
CSL_INTERFACE
csl_unit u2{
  - ifc ifc2l, ifc2r;
  - u2(){
    - ifc2l.reverse();
    - ifc2r.reverse();
  - }
};
csl_unit u3{
  - ifc ifc3l, ifc3r;
  - u3 () {} };
u[[1-3]].ifc[\1].reverse();
u[[1-3]].ifcu[\1]r.connect(u[[2-3]|{1}]).ifc[\2]l;
csl_interface ifc{
  - csl_port a(input);
  - csl_port b(input);
  - csl_port c(output);
}
csl_unit u1{
  - ifc ifc1l, ifc1r;
  - u1(){
    - ifc1l.reverse();
    - ifc1r.reverse();
  - }
};

---
Using interfaces
csl_interface ifc{
  - csl_port a(input), b(input);
  - csl_port c(output);
  - ifc () {} };
csl_unit unit{
  - ifc ifcl,ifcr;
  - unit(){
    - ifcl.reverse();
  - }
};
csl_unit top{
  - unit u0, u1, u2;
  - top(){
    - u[[0-2]].ifcu[\1]r.connect(u[[1-2]|{0}]).ifc[\2]l;
  - }
};
u2
u3
u1
x
y
z
x
y
z
x
y
z
x
y
z
x
y
z
x
y
z
ifc1l
ifc1r
ifc2r
ifc3r
ifc2l
ifc3l

---
CSL_SIGNAL_GROUP
Signals can be grouped together to form a single object which is more efficient to manipulate than performing the same operation on individual signals.
Signals can be added to vectors which get values in algorithmic or behavioral simulators.
Signal groups and vectors can be used later to construct testbenches.

---
CSL_INSTANCE_TREE

---
CSL_AUTOROUTER
CSL autorouter is a CSL language construct that allows the designer specify:
  - portions of the specification that should be processed/skipped by the autorouter tool
  - autorouter directives
  - autorouter options

---
CSL_AUTOROUTER
The cslc auto router automatically connects signals in the following cases:
  - connect by name - inference when the names of the connection endpoints are the same.
  - csl connection statement - explicit connections specified by the connect method

---
CSL_AUTOROUTER: Connection by name
//CSL code
csl_unit a{ csl_port x(input);
a () {} };
csl_unit b{ csl_port x(input);
b () {} };
csl_unit c{ csl_port x(input);
c () {} };
csl_unit middle{ csl_port x(input);
a a0;
b b0;
middle () {} };
csl_unit top{ csl_port x(input);
middle middle0;
top () {} };
//generated Verilog code
module top(x);
input x;
middle middle0(.x(x));
endmodule
module middle(x);
input x;
a a0(.x(x));
b b0(.x(x));
c c0(.x(x));
endmodule
module a(x);
input x;
endmodule
module b(x);
input x;
endmodule
module c(x);
input x;
endmodule

---
CSL_AUTOROUTER: Connection by name
x
top
middle
x
x
x
c
a
b
x
top
x
middle
x
x
a
c
b
x

---
CSL_AUTOROUTER: Connection rules
Connecting a port of the parent unit to a port in the child unit: no wire is created
Connecting two ports belonging to sibling units: only wires are created
Connecting ports on different levels of the hierarchy: autorouter will infer ports for each level until it reaches the scope of the nearest common container where it will infer wires.

---
CSL_AUTOROUTER
//CSL code
csl_unit a{ csl_port x(input);
a () {} };
csl_unit b{ csl_port x(input);
csl_signal z(wire);
//no need to specifically turn on the auto
//router on a0 and a2 since it is on by default
a a0,a1,a2;
b () { a1.set_auto_router(off); } };
csl_unit c{ csl_port x(output);
c () {} };
csl_unit top{ csl_port x(input);
b b0;
c c0;
csl_signal y(wire);
top () { y.connect(a0.x); } };
a a2(.x(x));
endmodule
module a(x);
input x;
endmodule
//generated Verilog code
module top();
wire y;
b b0(.x(y));
c c0(.x(y));
endmodule
module c(x);
output x;
endmodule
module b(x);
input x;
wire z;
a a0(.x(x));
a a1(.x(z));

---
1st variant
top
b0
a0
autorouter(on)
        x
a1
autorouter(off)
        x
a2
autorouter(on)
        x
z
c0
c0
autorouter(on)
x
x
autorouter(on)

---
Selective autorouting: before routing
2nd Variant
autoroute(on)
autoroute(off)
top
b0
a0
        x
a1
        x
a2
        x
z
c0
c0
x
x

---
Selective autorouting: after autorouting
top
b0
a0
        x
a1
        x
a2
        x
z
x
c0
c0
x
x

---
CSL Register File Class
csl_register_file

---
CSL_REGISTER_FILE
CSL register file is a CSL language construct that allows designer to specify register files
the register file can be constructed from:
  - flip-flops (size < 1kb)
  - SRAM memory (size > 1kb)

---
CSL_REGISTER_FILE
csl_register_file class has methods that allows the designer to tailor the register file for different applications and architectures:
  - read/write optimizations
  - processor architecture
  - Special requirements for computer architecture:
  - valid bits
  - operand bypassing

---
CSL Instruction Set Architecture Tool
CSL instruction set architecture (ISA) is used to specify the instructions that the system can perform and the format for each instruction
The specification of the instruction set will include :
Opcodes
fields with specific significance
specification of the instruction set will also specify the hardware elements controlled by the instruction set.

---
Instruction Set Architecture
The cslc will convert the CSL Instruction Set Architecture (ISA) specification into the following components:
  - microcode documentation
  - microcode compiler/assembler
  - generates Verilog and C++ ISA decoder
  - generates Verilog and C++ ISA field selects
  - Verilog or C++ microcode micro engine or processor
  - Verilog or C++ microcode controlled related datapath elements and/or signals to control
  - datapath elements

---
CSL Instruction Set Architecture Tool
The CSL ISA is based on the following classes:
csl_isa_field
csl_isa_element

---
CSL_ISA hierarchy
ISA
Formats
Instruction
Sets
Instructions

---
Derived CSL Instruction Format
Instruction Format
op
op
rd
rd
op2
op2
imm22
imm22
p
op2
cc0
cc1
disp19
op
cond
op
a
0
rcond
op2
d16hi
p
d16lo
a
op
op2
cond
a
disp22
Opcode
Opcode
Operation
Operation
Opcode
Opcode
Operation
Operation
Opcode
Opcode
Operation
Operation

---
CSL_ISA_ELEMENT
CSL ISA instruction class allows the designer to define the instruction set of an ISA
An instruction is a single operation of a processor within a computer architecture.
The types of instruction allowed are defined and determined within the ISA.
CSL ISA formats specify the field names in the instructions and which of these are decoded to generate data (operands) and control signals for the datapath
instruction formats are defined using cells (fields)
Different formats can be associated to different instructions

---
Tools description

---
CSL Verification Components
CSL verification components are CLS data structures used in the verification step of the design flow
verification components are use together with CSL Testbench tool

---
CSL Verification Components
CSL verification components (VC) tool can be used to specify
  - VC characteristics
    - format
    - VC set size
    - id
    - prefix
  - source/destination
    - file
    - C/C++ simulator
    - RTL simulator
  - associated elements
  - timing and control signals
  - associated events

---
CSL Verification Components
Verification components can be used for verification in the following different ways:
  - load expected verification components into the testbench memory and compare it with the design under test (DUT) output at runtime
  - store the DUT response in to a file and then compare with the expected verification components file

---
CSL Verification Components
CSL verification components are of two types
csl_vector
csl_state_data

---
CSL_VECTOR
a verification vector is a set of values associated with a set of signals.
the order inside the vector is determined by the associated order of signals
csl_vector can be used to specify:
  - the stimulus vectors
  - the expected vectors

---
CSL_VECTORS
Using CSL we can specify:
  - signal list to be included in the vector format
  - data radix (binary, decimal, hex)
  - trigger events
  - source/destination (file, C/C++ or RTL simulator)
  - prefix
  - size of the vector set
  - control and synchronization signals (clock, reset)
  - error limit number for verification
Note: signal and port constructs like csl_list, csl_signal_group and csl_interface can be used in order to structure and simplify source code

---
Generation of stimulus vector file
csim
vec
gen
stimulus
 vector
file
unit

---
Generation of stimulus vector file
csim
unit
vec
gen
expected
 vector
file

---
CSL_STATE_DATA
a state data is an array that contains the state of all memory cells inside a design under test (DUT)
memory cells can be
  - flip-flops
  - registers
  - register files
  - FIFOs
  - memories

---
CSL_STATE_DATA
Using CSL we can specify:
  - memory cell list to be included in the state data format
  - data radix (binary, decimal, hex)
  - trigger events
  - source/destination (file, C/C++ or RTL simulator)
  - prefix
  - size of the state data set
  - control and synchronization signals (clock, reset)
  - error limit number for verification

---
CSL Testbench Tool
csl_testbench
csl_clock_gen
csl_pattern_gen

---
CSL_TESTBENCH
CSL testbench tool is used to create an operating environment around the design under test (DUT).
To test consists in verifying that DUT provides correct outputs for the given inputs.
Outputs provided by the design when driven by a given set of inputs should match the expected outputs known to be good.
CSL testbench tool allows a DUT to be tested starting from an initial state specified by a csl_state_data element

---
CSL_TESTBENCH
The stimulus inputs and expected outputs are:
  - generated by another model:
    - C/C++ model
    - RTL model
  - acquired from hardware known to work correct
The stimulus vectors reflect all possible input combinations the design should be able to handle
The expected vectors contain all the outputs the design should yield.

---
Testbenches
Testbench
Verilog
DUT (Design Under Test)
(E)
Vectors initializations
State stimulus
csl spec file
cslc
(D)
(C)
mem
mem
Expanded state
Vectors
(B)
(A)
C++ simulator

---
Testbenches
expect vector
compare events
error ++
match ++
total ++
output vector

---
CSL_CLOCK_GEN
CSL clock generator class is used in the case there is more than one clock generator in the testbench
The tool can be used to create clocks with different characteristics:
  - time base (ps, ns, us, ms, s)
  - period (in units of time base)

---
CSL_PATTERN_GEN
CSL pattern generator tool is used to generate signals following defined patterns
Different base time can be specified for generated signals
Reset command can be specified to indicate the reset of the pattern-based generated signal

---
CSL_MEMORY_MAP
Memory maps are defined to enable the use of symbolic names for memory elements.
Memory elements can be

---
CSL_MEMORY_MAP
Memory maps are used by
RTL team
C++ chip simulator team
Test team
Software driver team

---
Memory map. Mappable hardware elements

---
Memory map: inputs and outputs
documentation
PDF
csl
lib
.csl
pp
documentation
HTML
cslc
csl pp
.csl
C++
generated
code
RTL
generated
code

---
Memory map. Hierarchy
mtop
m4
m0
m2
m3
m1

---
  local
address
  offset
 global
address
  base
0
500
31
531

---
mem_a
mem_b
addr
addr
35
0
31
67

---
0
0
base_0=0
15
15
0
16
base_1= base_0+16
31
47
   global
addresses
    local
addresses

---
reserved_ mmap
0x1000
0x3FFF
0x7FFF
0xFFFF

---
CSL Tools
Inter-
connect
Testbench
Buses
Register
Memory
map
Register
file
CSL
Pipeline
ISA
Memory
controller
MBIST
Verification
components
FIFO

---
Registers
CSL_register offers following register types:
  - Action Register
  - Atomic Register
  - Counter Register
  - Control Register
  - DFF Register
  - Event Register
  - Interrupt Register
  - LFSR Register
  - Statistic Register
  - Semaphore
  - Status Register
  - Program counter

---
Special signals
CSL_register commands allow easy configuration of register by adding general purpose or special control signals:
  - clk – clock
  - set/reset – set/reset the register
  - clr – asynchronous clear
  - en – enable
  - in/out – data in/out
  - inc/dec – increment/decrement
  - init – initialize register
  - rd_en/wr_en – read/write enable
reset set
in out
reg
rd_en wr_en
inc dec
clk
init en clr

---
Synchronous 2-bit register
csl_register reg_d{
reg_d() {
set_width(8);
set_type(register); }
};
csl_unit u{
csl_port d_in(input,2),
d_out(output,2), clk(input);
reg_d reg_d0(.clock(clk),.reg_in(d_in),.reg_out(d_out));
u () {
clk.set_attr(clock);
}
};
        out
in
reg_d
clk
2
2

---
Synchronous 2-bit register
csl_register cntr {
cntr() {
set_type(counter);
set_width(8);
add_logic(reset);
add_logic(count_amount,1);
add_logic(count_direction,up); } };
csl_unit u{
csl_port d_in(input,4),
d_out(output,4), clk(input),en(input);
reg_d reg_d0(.clock(clk),.d_in(d_in),
.d_out(d_out),.enable(en));
u () { clk.set_attr(clock); }
};
        out
in
reg_d
clk
2
2

---
Synchronous bidirectional 4-bit counter
csl_register cntr {
cntr() {
set_type(counter);
set_width(8);
add_logic(reset);
add_logic(count_amount,1);
add_logic(count_direction,up); } };
csl_unit u{
csl_port d_in(input,4),
d_out(output,4), clk(input),en(input);
reg_d reg_d0(.clock(clk),.reg_in(d_in),
.reg_out(d_out),.enable(en));
u () { clk.set_attr(clock); }
};
reset
d_in d_out
  cntr
dir
clk
        en
4
4