Chip Specification Language (CSL) and Compiler (CSLC)

Overview
We will describe a high level language and a compiler that is used to specify and create computer chip designs.

Generate equivalent constants and functions in different languages.
I claim that a high level language can be used to generate equivalent constants and functions in different languages. The equivalent code in different languages eliminates parallel code streams and guarantees that the different teams are using the same numbers and methods. This claim applies to all CSL or high level language specifications which are compiled and which generate code and documentation in different languages and forms from the same original specification in the claims below.

CSL Interconnect Specification
CSL facilitates the architecture, design, implementation, simulation, generation of test, generation of software tools and documentation of complex chips.

A chip is a set of functional units. Units have interfaces (ports), which are connected to other ports or to the pads of the chip (the system interface). The functional unit hierarchy and interconnections are described using CSL.

I claim the CSL is a high level language used to capture a chip design's architecture, design implementation, and verification infrastructure details. Register transfer level language (RTL) describes computer designs at a logic level. CSL describes cross functional areas such as the chip's memory map, the chip's instruction set architecture, the chip's hierarchy and interconnect, the aggregate structures such as special registers, FIFO's and register files, connections between simulation models and the test benches used to verify designs and the designs. Moreover, CSL libraries implement more complex aggregate structures such as networks on a chip, SOC fabrics, hierarchical MBIST

CSL is an object oriented language that uses many of the same syntax elements as C++ (classes, constructors, inheritance) and additional syntactic sugar borrowed from RTL languages (formal to actual mappings, bit ranges).

I claim the CSL compiler, CSLC, parses CSL files, elaborates the model using auto gen tools to create the implementation model, checks the CSL model for correctness, and finally generates RTL, C++, and documentation.

One of the main features of CSL and cslc is the generation of the same information in multiple output languages. This reduces and/or eliminates the “book keeping” required to ensure that the different language files for a particular aspect of the design contain the same information.

A cross functional area is defined as a set of related functions which are defined across many functional units. Memory maps affect many functional units on a chip. The hierarchy and interconnect on a chip affect many units. The instruction set architecture (ISA) affects many units and defines to a certain extent the pipeline(s) on chip. These cross functional areas need to be specified in an architecture, implemented by designers, tested by the verification team, used by the software team, and documented by the documentation team. The cross functional areas are therefore a shared specification used across the chip and by many different teams.

A shared specification should have one source to avoid confusion and misunderstandings, eliminate duplication of the source in documents and source code, and to facilitate rapid changes to the specification which can be immediately propagated throughout the design team. A single programmatic source for the specification achieves all of the above goals.

I claim the single CSL source for the specification can be checked by a compiler for specification correctness.

In addition cross functional areas are related to each other. This will be described later in this document. Relationships between cross functional areas in the past have been checked by generating code, checking for compilation errors and simulating and checking for simulation errors. This process is expensive in terms of engineering time, computing time and resources, and EDA licenses for RTL simulation tools. Finding errors in the specification prior to simulation is facilitated by using a specification language (CSL), which is checked by a specification compiler (CSLC).

I claim that relationships between CSL cross functional areas can be checked for correctness.

CSL Memory Map Specification
The functional units communicate with one another and with the system and software running on other chips via the interfaces. The functional units have address maps which are written to or read from by other functional units or by software. An address map associates an address or address range with a state element or aggregate state element respectively. Address buses in conjunction with operation (read/write), control and data lines write or read data to or from the state elements in the address map. Address maps for chips can be either flat (linear address range for entire chip), hierarchical (a unit address to select a functional unit and a subsequent local address to select a local state element), or virtual where the unit address and the local address are combined in a single address bus operation. Address buses may be implemented using different topologies such as a bus, token ring, tree, or mesh.

A major problem arises when the functional and alternate models are written in different languages (unconnected tools). The use of different languages creates a need to assure that address map constants and functions are the same in each language.

I claim only a specification language such as CSL can automatically generate consistent address map constants and functions.

CSL enumerated Type Specification
Enumerated types which are identical to C++ enumerated types may be specified. Enumerated types may be associated with signals and fields.

Other high level and RTL languages do not generate decoders from enumerated types associated with hardware elements and connectivity objects (e.g. wires).

I claim CSL generates decoders from enumerated types associated with fields in hardware elements and connectivity objects (e.g. wires).

I claim that the decoders are constructed correctly by the CSL compiler.

I claim that constants in functional languages such as C++ are generated correctly by the CSL compiler and can be used to construct software which aligns information (values) in the correct position associated with the field that is connected to the decoder.

CSL Field Specification
Fields are bit ranges that are named objects. Fields have an upper and a lower bit range index. The field has a name. Decoders can be automatically generated from fields associated with connectivity objects and register or other state elements and fields with enums associated with connectivity objects and register or other state elements . Other languages do not generate decoders from fields. The decoders are constructed correctly.

I claim that a high level language field may be joined with other fields using a linked list like set_next or set_previous operation and that the linked list may be added to connectivity objects and register or other state elements. Note that there are other applications of the linked list of fields and this claim should not be limited to just associating linked lists of fields with connectivity objects and register or other state elements

I claim that a high level language field can be used to construct a hierarchical tree of fields and that the hierarchical tree of fields can be implemented using different programming methods but not limited to trees or inheritance. Note that there are other applications of the hierarchical tree of fields and this claim should not be limited to just associating linked lists of fields with connectivity objects and register or other state elements

I claim that high level language hierarchical field specification are used in the design of instruction sets.

I claim that high level language enumerated type can be associated with a high level language field(s).

I claim that high level language field specification associated with high level language decoder generation method and that decoders can be automatically generated from high level language field specification.

CSL instruction set architecture Specification
Functional units and alternate models (e.g. a simulation model) may execute programs which are built from an instruction set architecture (ISA) specification written in CSL. The instruction set architecture is described using CSL.

The functional units and the external model (e.g. a simulation model outside of the functional unit) that implement the instruction set architecture, and execute programs written in the instruction set architecture assembly language, need to use the same set of instruction formats, instruction field definitions and enumerated type values.

A major problem arises when the functional and alternate models are written in different languages. The use of the shared constants in the different languages by the different teams require that the same values be generated in the different languages. The constants describe the width and position of each field in each instruction format and instruction and associated functions. Additionally functions are auto generated which insert and extract values to and from the instruction words. The constants are automatically generated from a specification language such as CSL.

I claim that a high level specification language can be used specify constant values in functional areas and that those constants in those functional areas are related to other constants in other high level specification language functional areas and that the combination of the areas and constants in the high level specification can be compiled and the compiler can generate constants in different languages and in different files for use by different teams on a chip design project in order so that the teams have the same constant values represented in different languages.

I claim that a high level language description of an instruction set architecture in a tree or inheritance hierarchy or any other hierarchical data structure can be compiled and the compiler can automatically generate RTL and alternate model languages which eliminates inconsistencies between the functional unit and alternate models.

I claim instruction formats and instructions can be built using hierarchies of fields.

I claim enumerated types are created to specify the opcodes and other sets of select values for fields in an instruction set. The enumerated types are associated with a field in an instruction format or instruction. Instruction formats may be inherited by other instruction formats or instructions.

I claim ISA's specified by a high level language description can be associated with register specified by a high level language description .

I claim decoders can be generated for fields and enums associated with registers specified by a high level language description which have an associated ISA's specified by a high level language description.

The ISA has two types of information that are used in the processor data path. 1. The encoded information such as opcodes. 2. The selectors such as register file address fields. The encoded information is decoded by decoders automatically generated by CSL. The “selectors” are fields. The fields are connected to signals. The signals are created by using a hierarchical identifier to refer to the signal name and then the hierarchical path to the field in the instruction. The hierarchical path includes the instruction name and the field name.

Example
csl_signal [31:0] ir;
ir.associate_isa(isa);
csl_signal alu_opcode(ir.isa.alu_instruction.alu_opcode.get_width()) =  ir.isa.alu_instruction.alu_opcode;
selects the alu_opcode field from the signal.

ISA's contain two types of elements instruction formats and instructions which use the instruction formats. ISA elements are derived from a common base format which specifies the width of the ISA instruction formats and the name of the ISA. Sub ISA instruction formats can be inherited from parent ISA formats. ISA instructions inherit an ISA instruction format. Instruction formats and instructions contain ISA fields. An ISA field is a named bit range with a width. Fields are placed into instruction formats and fields in either absolute positions or relative to other fields or the left or right edge of the instruction. Since there is a hierarchical relationship between the ISA instructions formats and the ISA instructions and there is one root format a tree of ISA instructions formats and the ISA instructions may be constructed to represent the ISA. The ISA tree may then be analyzed to form instruction decoders. A hierarchical identifier is a set of names in scope holders separated by a period. An hid forms a hierarchical path to an element in the ISA. Hierarchical identifiers (hid) can be used to access any instruction format, instruction, field, or enum in the ISA. The hid is a reference to an object in the ISA. Operations such as decoder or signal generation can be performed using the hid information. ISA fields have a type. The type information is used to control the generation of hardware in the control and data paths. the type information can also be used to check the usage of the hid's in the designer's custom code. For example, the type information may indicate that the field is a selector which means it may be used as a mux select. Or the field may be a branch address so it must be used as an input to a branch address mux, or the field is an opcode so it must be decoded and used to enable or select objects.

CSL Register Specifications
I claim a high level language can be used to specify registers.

I claim that the registers can be added to the high level language memory map specification. The registers can be addressed for read and/or write operations. The CSLC generates hardware which selects the registers for read and/or write operations. instruction set architecture's can be associated with registers. Fields in registers can be defined

I claim that a high level language register specification can be associated with other high level specifications such as but not limited to connections, memory map locations, decoders, enumerated types.

I claim that a high level language register specification can be used as a building block to construct aggregate structures described in the hig level language.

CSL Decoder Specifications
I claim CSL can be used to specify that decoders be generated from signals, registers, fields, and instruction set architecture's. The fields can reside in signals or registers. Decoders can be generated from registers with instruction set architecture's associated with them. The decoders can have enable signals which qualify the decoders outputs. Decoders can be generated to decode the memory addresses using the CSL memory map specification.

CSL Pipeline Specifications
Digital pipelines can be specified using CSL, checked for correctness by a compiler, and the compiler can then generate code in different languages for use by members of a hardware and software team. The functional units contain logic which implements an algorithm or instruction set architecture as a digital pipeline. Pipelines contain pipe stages. The pipe stages in a pipeline share signals such as clock, reset, stalls, valid, data, and control signals. Moreover, there are signals common to the connection between each pipe stage such as data, valid, and control.

I claim digital pipelines can be specified using a high level language, the high level language language specification can be checked for correctness by a compiler, and the compiler can then generate code in different languages for use by members of a hardware and software team.

In fact sets of data, valid, and control signals can be modeled as three separate pipelines whose latencies, clock, reset, and stalls are connected identically in each pipeline. Branches and merges of the three different types of parallel pipelines requires careful design and any changes to one pipeline must be mirrored in the two other pipelines. The user must use the CSL pipeline mirroring commands to associate pipelines. Register leaks (data loss due to a pipeline continuing to execute when a downstream pipe stage is stalled) or register data duplication (as a result of failing to qualify a valid bit with a down stream stall signal) are all problems faced by designers of digital pipelines. Pipeline design and subsequent changes can be simplified by specifying the digital pipeline in a CSL specification. The specification can be checked by cslc for the above mentioned problems and the designer can make the necessary changes. CSL pipelines can be combined with interconnect aggregate structures (signal groups) to create maintainable pipelines where the definition of the signals in the pipeline is done once in a signal group and the signals are then added to the pipeline from a starting pipe stage to an ending pipe stage. The pipeline specification can be checked for correctness by CSLC, the CSL compiler.

Valid bit qualification on stall and valid bit cancellation on pipe stage branch are just some of the pipeline properties checked in the CSL compiler.

I claim digital pipelines can be specified using CSL, checked for correctness by a compiler, and the compiler can then generate code in different languages for use by members of a hardware and software team.

I claim digital pipelines can be specified using a high level language can specify that stall signals be correctly connected to all state elements automatically.

I claim that the stall signal digital pipeline specification using a high level language can be checked for register leaks and duplicate data in the pipeline.

I claim that the valid bit signal digital pipeline specification using a high level language can be checked for correct qualification in branch and merge points and when the pipeline is connected to stall signal(s).

I claim that the a high level language pipeline specification with branch points can be compiled and that the down stream merge point can have a checker to verify that only one branch has a valid bit at any point in time at the merge point .

I claim that the digital pipeline specification using a high level language can be used to create copies of the pipeline for use by not but not limited to the generation of parallel control, data, and valid pipelines.

I claim that signals which contain many fields or group of signals which are pipelined can be connected to each input and output of the pipe stages in the pipeline automatically and that the signals are automatically named.

I claim that hierarchical identifiers can be used to access parts of signals in pipelines which contain many fields at any point in the pipeline.

I claim that a high level specification language can be used to specify the prefixes and and suffixes for automatically generated pipe stage signals. One example of automatic suffix generation from a high level language specification is the creation of suffixes which have a pipe stage number for the automatically generated signals in each pipe stage.

I claim that the high level specification language pipeline specification can be checked for correctness and can be connected to other high level specification language elements such as but not limited to registers, register files, interconnect, and FIFO's.

I claim that a high level language pipeline specification have an option to generate clock gated micro pipelines which turn on the down stream pipe stages one cycle in advance to avoid races between clock and data and that there is a two/three cycle “window” of pipe stages in the pipeline and that the micro clock gating reduces the power consumption on the chip. Stages which do not have valid data as indicated by a a valid bit associated with data in each pipe stage are shut off. Stages downstream from the current valid pipe stage which do are off are turned on one cycle in advance in order to avoid the race between clock and data.

CSL FIFO Specification
I claim CSL FIFO is used to specify FIFO's. CSL FIFO specifications are converted to RTL and alternate modeling languages such as C/C++.
Claims to add

I claim that a high level language spec for FIFO that includes the following and the feature is added to the generated model
bypass generation
fifo added to memory map
synchronous design
asynchronous design
low/high water marks
full/empty pointers
push and pop signals
stall calculation based on time to stop FIFO

CSL Register File Specification
I claim CSL Register File is used to specify Register File 's. CSL Register File specifications are converted to RTL and alternate modeling languages such as C/C++. The Register File specification is used to specify the typical register file configuration options such as the number of write and read ports, create connections to registers external to the Register File by in the Register File address space, connect individual registers to the Register File inputs/outputs, and create bypass signals.

I claim that a high level language spec for FIFO that includes the following and the feature is added to the generated model
Claims to add
bypass generation
external registers
connect individual registers to signals or ports
rf added to memory map

CSL Registers
claims
registers with certain features list a few but limited to the list
spec for certain types of registers
fields can be associated with registers
registers can be connected to connectivity objects

CSL Clock Tree
Andrei add claimsa
All state elements can be connected to a clock in the clock domain
Clock domains can be set for certain hierarchies
gated clocks can be specified
different types of clock gates can be specified
clock trees can be built
clock trees and user logic can be checked for races.

CSLC object model generators
I claim CSLC contains object model generators which are used to convert concise language specifications into fully elaborated models. The generators include the auto router and the auto mapper. The auto router “routes” point to point connections in different hierarchies. Intermediate ports and formal to actual mappings between the connection end points are created.

The user can mark state elements such as registers, register file, and memories in units to be included in the memory map. The auto mapper elaborates the memory map specification by visiting each unit in the hierarchy and adding elements in the units which have been marked as belonging to the memory map. The type of the memory map (flat, hierarchical, or virtual) determines the addressing scheme that the auto mapper uses to create the memory map.

I claim that the high level language can specify a point to point connection between two or more end points in two or more units separated by one or more units and that an auto router can automatically create the connections between the two or more end points in the intermediate units.

I claim that the high level language can specify that there are memory elements in a unit such as but not limited to registers, register files, memories, and fifos and that each memory element that is to be included in the memory map is marked and optionally has associated memory map attributes added to the memory element and that the auto mapper walks through the memory map specification which can be in text or converted to symbolic form and that auto mapper generates the memory map in the object model of the compiler.

I claim that an auto mapper can automatically create the memory map from a high level language specification.

Cross functional relationships
CSL types have relationships that create a system for specifying chip
designs that has not been previously available in one language and
compiler. These relationships can be checked by the CSL compiler.

signal<->field

field<->enumerated type
field<->decoder generation

interconnect_connectivity_objects<->vector specification

fifo<->state data
memory<->state data
register_file<->state data

vector<->test bench
state data<->test bench

memory map<->interconnect
memory map<->registers

registers<->field
registers<->instruction set architecture
registers<->interconnect

instruction set architecture<->decoder generation

pipeline<->interconnect
pipeline<->register file
pipeline<->fifo

CSL features
high level language for specifying the relationships between different
design components

CSLC Specification Checkers
i claim CSLC includes specification checkers which verify that the CSL specification are correct. It is not enough to check individual cross functional specifications since the individual cross functional specifications affect each other. Checks between the individual cross functional specifications must be made.
- interconnect-checks for correct connections between modules based on type, direction, and width
- pipeline-checks for data leaks, stalls, and resource deadlocks
- memory map-checks for duplicate addresses,...

CSL Cycle Based Functional Simulator specification
I claim that compiling a high level language specification and generating the skeleton for a C++ cycle based simulator in conjunction with a set of C++ cycle based library files and a set of user generated functional logic comprise a maintainable golden simulator that generates vectors and state data to be used in the verification of designs under test in automatically generated test benches. Furthermore, the C++ simulator can be used to verify diagnostic tests (write, read, compare) which then can be run using a test bench in a stand alone mode to verify the RTL design under test.

I claim that the generated C++ simulation skeleton contains a method for including user generated code including but not limited to an include file mechanism where inline include statements include users defined code in the included files.

I claim that the generated C++ simulation skeleton contains an API which the user can “write to” to connect the user generated functions with the compiler generated functions and library functions.

I claim that the generated C++ simulation skeleton instantiate memories specified with the high level language and that there are generated methods for writing and reading the memories in a single transaction mode and a “side door” method for writing and reading parts of or the entire memory in a parallel mode.

I claim that high level language specification can describe vectors that are created by the C++ simulator and the compiler can generate the C++ vector writers to generate the transaction level vectors which are then used to stimulate the design under test and also to compare against the design under test outputs.

I claim that the vector writers can generate either cycle accurate vectors or transaction accurate vectors or pipes tage and transaction (models the latency through the pipeline but the actual logic is not in the exact same pipe stage in the C++ model as the RTL design under test) accurate level vectors

I claim that high level language specification can describe vectors that are read by the C++ simulator and applied to chip or unit level interfaces in the C++ simulator and that the compiler can generate the C++ vector readers to generate the transaction level vectors which are then used to stimulate the C++ simulator and also to compare against the C++ simulator chip and unit level outputs.

I claim that the vector readers can read either cycle accurate vectors or transaction accurate vectors or pipe stage and transaction (models the latency through the pipeline but the actual logic is not in the exact same pipe stage in the C++ model as the RTL design under test) which are then used to stimulate the C++ simulator and also to compare against the C++ simulator chip and unit level outputs.

I claim that high level language specification can describe state data in the the C++ simulator and the compiler can generate the C++ state data readers to load the state data with initial state and generate the test bench support code to load the RTL design under test memories.

I claim that high level language specification can describe instruction memories and other storage units in the chip which contain executable instructions in the the C++ simulator and RTL design under test and the compiler can generate the C++ state data readers to load the state data with instructions in numerical format including but not limited to binary and generate the test bench support code to load the RTL design under test memories.

I claim that the generated C++ code can be compiled by a standard C++ compiler to create an executable which which when executed will simulate the chip using cycle based simulation.

I claim that the cycle based simulation will generate vectors which can be used to stimulate and test the RTL design under test.

I claim that the C++ cycle based simulator can use but is not limited to a single threaded mode of execution or a parallel multi threaded mode of execution or a or a parallel processor mode of execution

I claim that the high level language interconnect, state data, and test bench specifications can be compiled and the compiler can generate the C++ code for vector and state data writers which use a remote method including but not limited to a socket or other remote procedure call to connect directly to the test bench containing the design under test between threads on in a system or over a network or other communication mechanism

I claim that the high level language interconnect specification for the chip design can be compiled and the compiler can generate C++ code which uses a remote method including but not limited to a socket or other remote procedure call to connect one part of the simulator to another part of the C++ simulator between threads on in a system or over a network or other communication mechanism.

Memory map claims
A memory map can use one of the following address schemes: flat, hierarchical, or virtual

I claim that memory map test generators can be built automatically to test the entire address range using write, read, and compare tests.

I claim that the same memory map test(s) can be loaded using a side door method into the C++ simulator or the design under test.

I further claim that the same memory map test(s) can be loaded using vectors written into interface of the C++ simulator or the design under test.

Andrei add the rest of the memory map specification methods here to this claim

CSL Verification Specifications
Functional units may be verified by modeling the external drivers and receivers of the functional units interface (input and output ports) using alternate models built in different languages. The stimulus and expect vectors, and state data generated by the alternate models are used to verify the functional units.

I claim the software which performs the following tasks is generated by the CSLC from a CSL specification
vectors and state data are captured in the alternate model and sent to a file or connected to the functional unit test bench via inter-process communications.
- the file format is understood by the compiler via the vector and state data specification. A file reader is created in the test bench and the file is read into a memory in the test bench, which is the correct size to hold the vector
- a set of signals to control reading the vector/state data memory are created
- a set of signals to connect the stimulus memory to the functional unit under test are inserted into the test bench.
- a set of signals to connect the expect memory to the output comparators are inserted into the test bench.

The (automatic) connection of the vectors/state data generated by the alternate model to the functional unit in the test bench is fully automated. The CSL interconnect, vector, state data, and test bench specification are all defined in one language. The inconsistencies introduced by specifying these different components in different languages and using different tools to generate the RTL and alternate model code are avoided.

Moreover, the CSLC can check the CSL interconnect, vector, state data, and test bench specification in one tool and find inconsistencies between the various specifications.

Moreover, since the CSL interconnect, vector, state data, and test bench specifications have been read into one object model in a single software program, the CSL syntax supports reading objects such as the entire set of output signals from a functional unit using one statement. Using an aggregate connectivity structure which refers to a group of objects facilitates changes in the sub objects (name and width changes, additions and deletions) without having to change the upper level interface name which is used to specify that the output signals constitute a vector. The aggregate connectivity structure is routed from one unit to another unit. The underlying signals can be modified without affecting the routing since the aggregate connectivity structure is auto routed from end point to end point in the object model.

Verification of functional units on chips and of chips requires the development of vector and state data (two dimensional vectors from two dimensional memory elements) from a golden reference. Both stimulus vectors and expected vectors/state data are required in order to test the the design under test. The order of the signal values and the widths of the signals, the size of the memories need to be the same in the golden reference model (the functional simulator), the communication mechanism (file/socket), the mechanism in the test bench which applies the vectors to the DUT, loads the binary instruction files into the DUT instruction memories if present, and compares the outputs of the DUT with the expected vectors.

I claim that a high level language can be used to specify the order of the signal values, the widths of the signals in the vector, the event capture mechanism for the vector (cycle accurate or transaction accurate), the vector ID, Andrei add the rest of the vector specification methods here to this claim

CSL Memory
Andrei add the rest of the memory specification methods here to this claim

I claim that the high level specification language can specify the dimensions of memories that are used in the chip design.

I claim that the high level specification language can specify the relationship between the width of the ISA instruction word and the memory and then specify the width of the memory.

I claim that the high level specification language can specify the relationship between a memeory and a state data element and that the relationship between the state data element and the memory can be used to connect the state data writer to the memory.

I claim that the high level specification language can specify the relationship between binary files and the memory and that the memory load routine code can be automatically generated in different languages.

I claim that the high level specification language can specify the FPGA, memory compiler, or hand generated memories to use in the implementation model and that the equivalent memory will be generated in the function and structural models.

CSL producer consumer
Multi media chips move large amounts of pixels in matrices around chps and process the pixels. A producer unit will write the results of its operations to a memory and the consumer will read the memory. The data access patterns of the producer and consumer are fixed for a periodic operation. The producer write pattern may be different from the consumer read pattern. In other words the write and read orders for the producer and consumer respectively may be different. Programmable engines such as but not limited to counters or micro controllers can be used to write and read the memory.

I claim that the high level specification language can specify the write and read operation sequences for the memory and that the cslc compiler can generate the programmable or hard wired controllers which will generate the write and read address sequences to access the memory.

CSL Buses
Buses have a protocol and buses have a packet format.
I claim that a high level language can specify the packet format and that the packet format is made up of fields and which cycle the parts of the packet are assembled and the signals that make up the bus which carry the bits of the packet and that logic which implements the packet framing and deframing logic can be automatically generated.

I claim that a high level language can specify the protocol of the bus and that the protocol checkers can be automatically generated.

I claim that a high level language can specify the protocol of the bus and that the protocol hand shaking logic in the sender and the receiver can be automatically generated.

Automatic interconnect generation via high level design language description and an auto router
Modern designs have connections between connectivity objects (signals, port, signal groups, and interfaces) and containers (FIFO, Register Files, memories) and registers and functional logic. Connections between these objects can be made manually or using point to point connections and an auto router. A point to point connection is a set of end points in functional unit (ports, pins on combinational and state elements,...) that are connected to other end points. The rules for making the connections are defined in academic books. Driver contention is to be avoided. For example, a simple wire must have a one driver and one or more receivers. The connections between the end point can traverse through the design hierarchy (e.g. in Verilog RTL the design hierarchy is created with modules, module interfaces which contain ports, and instantiations of the module instances with formal to actual mappings connecting upper level signals and ports to the module instance's ports). Intermediate signals in modules may only be connected to other ports and signals and not to logic. The end points are connected to logic elements and state elements (flipo flips, registers, memories,...) The connections between the end points can vary depending on the architecture and design/implementation choices made by the architecture and design teams. Limitations in in the number of metal layers between block boundaries (referred to as “metal limited” in designer jargon) some times is discovered late in the design process and requires changes in the RTL design hierarchy and RTL module interfaces. Changes in the RTL design hierarchy ripple through to the test benches and simulator interfaces and vectors produced by the simulators for verification of the design under test.
Making hierarchy and interface changes late in the design cycle (project) can be very expensive and delay the development of the project. Automating the design hierarchy and interconnect generation process reduces the impact of design changes by facilitating rapid changes in the design hierarchy and interconnect without affecting the underlying functional logic of the design. Automation of the design hierarchy and interconnect generation process can be achieved by using a high level language to describe the point to point connections on the chip and the design hierarchy. The point to point connections on the chip are routed from leaf module to leaf module through the design hierarchy using a automatic routing tool to create the intermediate connections in the modules between the two endpoints.

I claim that a high level design language can specify a point to point connect between two or more objects and that a compiler can use the width detection via get_width() functions to determine the width of one or more connectivity object(s) in the point to point connect and the compiler can use the width information from the connectivity object(s) to set the widths of the connectivity objects in the point to point connect that are unknown, check the widths of all known widths, and to set the widths of the intermediate signals which are created automatically between the end points of the point to point connection.

I claim that a high level design language compiler can check for width mismatches between signals and other objects such as registers

I claim that a high level design language compiler can check field linked lists and trees for overlaps between adjacent fields in connectivity objects such as but not limited to signals using linked lists of fields and relative positions.

I claim that a high level design language compiler can detect width mismatches between a group of fields and connectivity objects that the fields are associated with.

I claim that a high level design language compiler can detect width mismatches between a field and the fields associated enumerated type (an enumerated type has a specified number of elements and the number of elements can be represented by a binary number which must be equal to or less than the field width).

CSL and user generated code.
I claim that the CSL generated code and the user generated code can be integrated to form one executable via include statements and other methods and that the two sets of code can be compiled by but not limited to a standard compiler such as gcc or an RTL compiler such as Cadence ncverilog.

CSL Network of processors
I claim that a high level language plus additional libraries can be used to specify a network topology which is used to send messages between processors using a network such as but not limited to a token ring, bus, mesh, tree, and star.

I claim that a high level language can specify the custom instructions used to send messages between processors using a network such as but not limited to a token ring, bus, mesh, tree, and star and that the user can add the additional logic to implement the functionality of the custom send and receive instructions.

I claim that a high level language specification for custom instructions used to send messages between processors using a network such as but not limited to a token ring, bus, mesh, tree, and star
can be used to create software tools which will compile the specification and then create a software tool to be used to compile the instructions into binaries that are then loaded into each processors instruction memory. The software tool will check the communication between the instructions and generate warnings and errors about communication problems in the user written instruction programs.

I claim that a high level language can specify the buffers used by each processor to store incoming and outgoing messages sent between processors using a network such as but not limited to a token ring, bus, mesh, tree, and star.

I claim that a high level language memory map specification can be used to create the address map used by each processor address the individual processors using a network such as but not limited to a token ring, bus, mesh, tree, and star.

I claim that a high level language memory map specification processor address map can be combined with other high level methods to create hardware to detect writes, reads and other operations sent to the individual processors using a network such as but not limited to a token ring, bus, mesh, tree, and star and that the hardware can write or read the memory map elements in the processor.

I claim that a high level language specification of the network such applies to networks on chip, networks between chips and other networks that can be specified using the high level language.

CSL Network of functional units
I claim that a high level language plus additional libraries can be used to specify a network topology which is used to send messages between functional units using a network such as but not limited to a token ring, bus, mesh, tree, and star.

I claim that a high level language can specify the custom instructions used to send messages between functional units using a network such as but not limited to a token ring, bus, mesh, tree, and star and that the user can add the additional logic to implement the functionality of the custom send and receive instructions.

I claim that a high level language can specify the buffers used by each functional unit to store incoming and outgoing messages sent between functional units using a network such as but not limited to a token ring, bus, mesh, tree, and star.

I claim that a high level language memory map specification can be used to create the address map used by each functional unit address the individual functional units using a network such as but not limited to a token ring, bus, mesh, tree, and star.

I claim that a high level language memory map specification functional unit address map can be combined with other high level methods to create hardware to detect writes, reads and other operations sent to the individual functional units using a network such as but not limited to a token ring, bus, mesh, tree, and star and that the hardware can write or read the memory map elements in the functional unit.

I claim that a high level language specification of the network such applies to networks on chip, networks between chips and other networks that can be specified using the high level language.

CSL Micro Engine Example
We will now describe an example design using CSL. Note that this is just an example of how CSL can be used to design a chip.

A network of application specific processors (micro engines) on a chip is a challenging design to implement. The application specific processors have general purpose instruction load/store/branch/logical/arithmetic instructions and additional specialized instructions that use an optimized data path to increase the effective computation power of the processor per compute cycle. A network of application specific processors combined with firmware can replace custom ASIC and VLSI pipelines. Applications which are not latency sensitive are ideal candidates for networks of application specific processors. Less engineering time and resources are required to build one application specific processor design, then instantiate it many times and write the associated firmware/microcode than it is to build a custom hardware pipeline. CSL can be used to implement the application specific processors pipeline, ISA, register file(s), interconnect, and memory map. The result is a skeleton of the design which is missing the functional unit logic. The generated skeleton includes the pipeline inference hardware, the connections between the pipelines, the instruction decoder, the extracted bit ranges from the pipelined instruction register, The designer then implements the functional unit logic. Functional unit logic include arithmetic, logical, load/store, and branch units. Software tools such as assemblers and compilers are automatically generated.

Design and figures to be added after CSL micro engine is completed.

CSL SOC Example

Design and figures to be added after CSL micro engine is completed.

Method for generating a network of application specific processors
Claim

User defines the application specific processor ISA, pipeline, memory
map, network topology, and ISA using CSL which is then compiled into
HDL/RTL simulation languages such as C++
cslc checks the ISA specification for errors
cslc checks the application specific processor pipeline for data and
control hazards and register leaks and data duplication problems
related to bad stall logic
cslc generates decoders from fields
cslc generates decoders from an enumerated type associated with field(s)
cslc generates an assembler from the tree representing the ISA specification
cslc generates assembly language documentation from the tree representing the ISA specification
cslc generates interconnect interface documentation on a module and per instance basis
cslc generates memory map documentation

ISA tied to the the custom interconnect
ISA built from users specification

Generated C/C++ code can be simulated in conjunction with other
C/C++ simulators by instantiating the functions. The generated
code supports both transaction accurate and cycle accurate modeling

Prior art
Tensilica/ARC patents on their extensible processors (the extend the functionality of their base processor design)

Clock trees
delay lines
wave shapers

DO WE NEED TO PUT CSL CODE HERE

DO WE NEED A FLOW DIAGRAM SHOWING THE STEPS TO CREATE AND COMPILE CSL CODE AND HOW THE CODE IS USED