# Introduction
CSL Register File tool is part of CSL design package which is used to specify register files which are common design units to be found in medium to high complexity designs. Register Files are especially used in Central Processing Units (CPUs) but any set of registers can be organized into register files in order to share data read/write and control logic.
The register file physical implementation can be specified indicating the use of either a memory array (SRAM) or individual flip-flops. The choice is based on the size of the memory array and the available technological options.
# Description
A register file contains a set of registers which are written and read using address, data and enable signals. The registers are addressable by read and write address lines. A read enable signal is used to access a register and return the contents of the addressed register, a write enable signal is used to store the data from the data input pins into a register.
All CSL register operations are supported inside of the register file including clear, set, enable, and reset.
The CSL language group operation can specify the assemble together of registers and fields within registers so that common operations such as clear or set can be performed on the registers.

dec

rd_addr1
wr_en
wr_data
wr_addr
rd_addr2
rd_data1
rd_data2

rd_en2
rd_en1
Figure1. A register file that permits two read operations in the same time and one write operatio.
The implementation logic of the register file can be a contiguous or non contiguous array and/or groups of discrete registers.
 Register File operations:
- write registers,
- read registers,
- shadow registers.
Register files for processor architectures have special requirements:
- valid bits,
- operand bypassing.
A valid bit may be optionally added to the register file. The register file will generate a valid bit whenever there is a read operation. A valid bit is used in hardware pipelines to indicate that the contents of the current pipeline is valid.
The register file’s registers can be connected to the inputs and the outputs of the register file. Fields within the registers can also be connected to the inputs or outputs of the register file. In a register file, individual registers can be named. The “named” registers can be accessed using the address and enable signal or read/written using a special signal connected from the named register to the register file output.
All memory input on map operations are supported inside of the register file. The register file memory map can have discontinuities or gaps in the address space. Read and write operations can optionally trigger events. Read operations can optionally generate valid bits. The range checker for the register file is implemented with a decoder. Specific instructions are available to assign an address to a register file.
Features
The CSL memory map specification is used to create memory mapped state elements that are addressable by other hardware units or by software through write or read operations.
The user can create registers files with multiple write, multiple read or with bypass features.
By default, the module's clock is automatically connected to the register file. If there are multiple clocks in the module in which the register file is instantiated then the CSL clock command has to be used to specify the clock name which is connected to the register file.
Address Collision Detection Logic -there is an option for a bad address checker which sets an error bit, captures the bad address in a register and generates an interrupt.
A register in a register file can be set to a constant value by setting the constant attribute to a value.
Register files are either instantiated inside of an RTL module using CSL commands or the register file is a stand alone module which can be connected to the design using the CSL interconnect commands
Register File configuration options:
- add read port,
- add write port,
- individual registers connected to an output,
- read/write registers from more than one source
- bypass
- add external registers
# Benefits
Using the CSL Register File the designer can:
- create an array of named registers,
- add the register file to the CSL memory map
- create register file type and instanciate it in different units,
- associate a global address and a local address to the register file .
- generate Verilog code, C++ code, and documentation (pdf or doc).
- associate state data object wiath a CSL register file
- connect a CSL register file to CSL connectivity objects(i.e. Signals, ports, signal group)
The user can create register files much easier and in a much structured way.
The contents of a shadow register file can be written in any order.
# Architecture Diagram
cslc / csl / lib / .csl / PDF / HTML / C++ code / RTL code / Figure 3. CSL Register File tool inputs and outputs.

# Dependencies
A register file can be implemented with register memory elements and can specify a group of bits in a register from the register file using CSL Field object.
# Supported formats
The register file supports the following input/output formats.
## Input:
CSL, Verilog, VHDL
## Output Generators Provided:
CSL, Verilog, VHDL, C/C++, HTML, PDF

To find out how CSL Register File can make your chip design more efficient; contact Fastpathlogic Sales today.

Table1. CSL Register File feature/benefits table
Register File Features	Benefits
Multiple reads and writes	Enables to read/write one or more registers at the same time
Serial and parallel data	Enables serial/parallel read input data and write output data from/to registers
Bypass Logic	Data can be read & written simultaneously (in the same machine cycle) from/to same register/memory location
Incremental design	Easy to modify initial specification with minimal design effort
Automatic clock signal connection	If there is one clock signal, it will be automatically connected
Address collision detection	Ability to check for bad addresses and generate an error message
Permission attributes	Enables to set read, write and/or shadow permission for any register in the register file