CSL architectural state
Connecting C++ simulators
and RTL testbenches

---
CSL architectural state
Expected architectural states must have a unit specified, using the CSL commands set_unit_name.

---
CSL architectural state
Architectural states are associated with a unit.
Architectural states are used by the testbench, but are not instantiated in it using CSL.
The default checker type is cycle accurate.

---
Architectural state
Architectural state are the values in a memory or set of memory type elements at a particular event (e.g. Clock or write enable).

---
Architectural state usage models
Architectural states can be written to a file.
Architectural states can be written to a socket.

---
Testbenches read architectural states
Testbenches read architectural states written from a file.
Testbenches read architectural states from a socket.

---
Architectural state types
The C++ simulator expected architectural states are compared against the corresponding DUT architectural state.

---
Events
Events are defined so that we can indicate points at which to turn on and turn off the architectural state recording. The architectural state is "captured" based on the verification architectural state type.

---
Events
In the C++ simulator each time that a architectural state event occurs the associated architectural state is recorded in a file. The verification architectural state recording is turned on and off based on another set of events such as after reset or a unit is enabled.

---
Cycle accurate architectural state
Definition: Cycle accurate-Logic is modeled in the C++ simulator and the architectural states are captured captured each clock cycle.

---
Transaction accurate architectural state
Definition: Transaction accurate-Logic is modeled in the C++ simulator and the architectural states are captured at a specific event.

---
Reset and architectural states
Architectural state is usually not captured prior to the assertion and de-assertion of reset.

---
Start and end events
A start event indicates when to start capturing architectural states. Reset is a typical start event.
An end event indicates when to stop capturing architectural states. End events include:
maximum number of architectural states captured
a complete video frame or stream has been sent through the simulator

---
Architectural state ID's
Architectural states are associated with a unique architectural state ID.
The unique architectural state ID is written to the architectural state file.
The testbench will check that the architectural state file to be read has the correct ID corresponding to the RTL ID and testbench ID.

---
Architectural state versions
Logic changes causes architectural states to change. Therefore architectural states are associated with an architectural state version.
The architectural state version is written to the architectural state file.
The testbench will check that the architectural state file to be read has the correct version corresponding to the RTL version and testbench version.