CSL/CSLC
The Front End Chip Architecture, Design and Verification Productivity Solution

---
Part 2
CSL Language

---
CSL Language
How do I get started? i.e. What's the min set of CSL language do I need to learn before I can specify my computer design?
How do I express my computer design? Is CSL rewrite rule programming? Or is CSL functional programming? Or is CSL procedural programming? Or is CSL object oriented programming? Tell the user.

---
The CSL unit:
  - Explain what a unit is. How do I write one? Credibility.
  - Examples of units
    - Interfaces, (??? usually interface is part of some circuit so explain when it is a separate unit)
    - Signals, (really wires???)
    - instances of CSL objects (do not use because “if I do not know about CSL objects instances do not matter”)

---
CSL_ENUM
an abstract data type that takes values in a finite set of identifiers
used for variables that do not have any numerical order
used for defining
types
identifiers
naming conventions
attributes

---
CSL_ENUM - examples
csl_enum packet_type{
green, blue, red
};
csl_enum prefix_type{
NO_PREFIX, PIPELINE_NAME, PIPESTAGE_NAME, PIPELINE_PIPESTAGE_NAME};
csl_enum e{ a=0, b=1, c=2};

---
CSL_LIST
csl_list is a language construct that allows the user to specify a
list of objects and use it as a single object
lists must contain object of the same type
lists are defined by user or can be generated by the regular expression preprocessor from regular expressions in the specification
lists are used in conjunction with list methods.
list can be used in foreach statements

---
CSL_LIST - example
Example 1. Set bitrange to a list of signals
csl_bitrange br_br(7,0);
csl_unit u_chip{
  - csl_signal a,b;
  - csl_list list(a,b);
  - u_chip(){
    - list.set_bitrange(br_br);
  - }
};

---
CSL_LIST - example
Example 2. Set enum to a field list
csl_enum e_enum{ADD,SUB};
csl_field field(5);
csl_field if_format {
field f_opcode(5);
  - field f_srca(5);
  - field f_srcb(5);
  - field f_dest(5);
  - csl_list f_list(f_opcode, f_dest);
  - if_format(){
    - f_list.set_enum(e_enum); } };

---
CSL_REGEXP
CSL language supports regular expressions (regex)
regexes cause CSL declarations and reference statements to expand into multiple statements
two main types
  - generate regex
  - search regex

---
CSL_REGEXP: Examples
//CSL code
for (int i=0; i<3; i++){
string col = “col_” + i + “_” + ”[[0-3]]”;
csl_signal col[13:0];
}
or
wire col_[[0-3]]_[[0-3]][13:0];
//generated Verilog code
wire col_0_0[13:0]
wire col_0_1[13:0]
wire col_0_2[13:0]
wire col_0_3[13:0]
wire col_1_0[13:0]
wire col_1_1[13:0]
wire col_1_2[13:0]
wire col_1_3[13:0]
wire col_2_0[13:0]
wire col_2_1[13:0]
wire col_2_2[13:0]
wire col_3_3[13:0]
wire col_3_0[13:0]
wire col_3_1[13:0]
wire col_3_2[13:0]
wire col_3_3[13:0]

---
Regular expressions

---
CSL_SIGNAL
Signals are CSL language constructs used to connect ports of different units
CSL signals are the equivalent of wires that connect different components of a system
CSL signals can be uni- or multidimensional
CSL signals are of different types and can have different attributes

---
Signal types
CSL signal types are similar to Verilog signal types
signal types are related closely to the hardware structure that is being described

---
CSL signal types

---
Signal attributes
Signal attributes are used to indicate special purpose signals
Signal attributes can be used by interconnect tool or autorouter in order to:
  - check signal compatibility
  - make special interconnects
  - allocate special hardware resources
  - generate specific hardware logic

---
CSL signal attributes

---
CSL_PORT
CSL ports are CSL language constructs that specify the interface through which it communicates with other units in the same design space.
CSL ports can have different direction types :
  - input
  - output
  - bidirectional
CSL ports can have same types as defined for signals

---
CSL_BITRANGE
CSL language construct that specifies
Easy way to specify multidimensional signals and ports
There are available different range declaration types:
  - lower_limit, upper_limit
  - width (implicitly lower_limit=0)
width can be a constant or numeric expression

---
CSL_BITRANGE
concatenation of bitranges is possible
relation to other bitranges can be specified using offset
there are available functions to set and get parameters of a bitrange