CSL/CSLC
The Front End Chip Architecture, Design and Verification Productivity Solution

---
Part 4
Design

---
Design example need a csl list and a cslc list
The design process has the following steps:
drawing the chip block diagram
defining memory map
creating hierarchy
creating interfaces for modules (or add???)
connect special signals (clock, set/reset)
make connections between modules

---
Design example
define instruction set architecture
generate library components to be instantiated in the modules
write logic for each unit and include in a leaf level unit generated from the interconnect
generate testbench and verification components for chip verification
write C++ model for the chip
simulate the design and compare RTL model outputs with C++ model outputs

---
suggestions
Mark steps as csl or cslc
Sets of slides for each step – same number and name so reader can track
All claims supported by example(s)
Explain source of info for each step
Explain what happens in each step
User doesn't enter verilog. If right verilog has no place here. If wrong explain why verilog is here because I thought we write spec using csl.

---
1. CSL Block diagram use same numbers and words as
in lists
chip
alu
im
rf
pc
id

---
2. Memory map
//a memory_map_page with an address range from 0 to 47 with an increment 1 and set the memory word width to 32-bits
csl_memory_map_page chip_mem_map_pg{
chip_mem_map_pg(){
add_address_range(0,47);
set_address_increment(1);
}};
csl_memory_map chip_mem_map{
chip_mem_map(){
set_type(hierarchical);
set_data_word_width(32);
}
};

---
3. Hierarchy
chip
pc
alu
rf
im
id

---
Hierarchy. CSL code delete verilog, not used in csl
// CSL code
csl_unit pc { pc() {}};
csl_unit im { im() {}};
csl_unit id { id() {}};
csl_unit rf { rf() {}};
csl_unit alu { alu(){}};
csl_unit chip {
pc pc0;
im im0;
id id0;
rf rf0;
alu alu0;
chip() {} };

---
Hierarchy
// Verilog code
module pc (); endmodule
module im (); endmodule
module id (); endmodule
module rf (); endmodule
module alu(); endmodule
module chip();
pc pc0( );
im im0( );
id id0( );
rf rf0( );
alu alu0( );
endmodule

---
4. CSLC Adding interfaces
chip
pc
alu
rf
im
id

---
Design example. Adding special signals
user drawing, cslc drawing? Misleading without supporting text
chip
pc
alu
rf
im
id
clk/reset

---
Design example: Program counter same ?
chip
pc
alu
rf
im
id
pc_0
pcr
clk/reset

---
Design example: Instruction memory
chip
pc
im
alu
rf
id
pc_0
im_1
instr_
mem
pcr
clk/reset

---
Design example: Instruction decoder
chip
pc
im
alu
rf
id
pc_0
im_1
instr_
mem
pcr
dec
clk/reset

---
Design example: Register file
chip
pc
im
alu
rf
id
pc_0
im_1
instr_
mem
pcr
dec
clk/reset
   rf
32x32

---
Design example: ALU
chip
pc
im
alu
rf
id
pc_0
im_1
+/-
instr_
mem
pcr
dec
O
<<
>>
clk/reset
   rf
32x32

---
Design example: Write logic
Show how to write using csl

---
Design example. Generate testbench and verification components

---
Design example. Write C++ model

---
Design example. Simulate the design