Relationships between CSL objects

---
Memory map sub-steps
Identify and mark map elements in units
set the ranges for the memory map elements
Create memory map either:
  - Manually
  - Automatically using the automapper

---
Interconnect sub-steps
Create hierarchy
Create interfaces for units (RTL modules)
Create signal groups for higher level interconnect
Connect special signals
Make connections between modules
  - Manually
  - Automatically using the autorouter

---
Design flow steps
Different designs are built using the same CSL components:
  - interconnect
  - memory mapping of components
  - defining logic for leaf units
  - generation of verification components
  - generation of decoders
  - generation of pipelines
  - generation of ISA'a and their associate signals

---
Design flow
Design flows are used to construct chips. Design flows are a sequence of steps that the design team execute during the chip design process.
Design flows are customized based on the type of chip that is being designed
The design process is divided in major steps. Each major step contain substeps that further refine the design process and can be used to customize and/or support different design flows.
CSLC and CSL language functional area support this refinement and customization of design flow to adapt the design process to different product categories

---
Design flow problem
A design flow describes the steps that a designer follows to implement a design
Writing a design specification is one of the steps in the design flow
Converting a written specification to RTL or C++ is subject to error
Inverting the process and writing the specification in a specification language which is then compiled, checked and then generates a set of programming files and documentation guarantees that all team members are using the same constant values, the same signal names with the same widths, the same verification vectors, and so on.

---
Define verification environment sub-steps
Generating the verification environment implies the following steps:
  - Define test vectors
  - Define state data
  - Define pattern generators
  - Define test events
  - Define testbench
  - Write C++ model for the design unit under test (DUT)
  - Include test vector and state data generators in the C++ DUT model to capture the vectors and state data

---
Code and documentation generation substeps
Generate RTL code (Verilog, VHDL, SystemC)
Generate C++ code
Generate documentation in html or doc format
Generate compilation reports
Generate design optimization suggestions

---
Design types
The CSL compiler can be used to develop different design types such as:
  - Graphics pipeline
  - Processor design
  - System on a chip (SoC)
  - Multiprocessors
Each of the above design types requires a different set of design steps

---
Design types
Different design flows are defined for different types of designs
Design flows for different types of designs share some common elements such as the design hierarchy, the interconnect, and the testbenches
Some designs may have an ISA while others may not.

---
Hierarchical design flow
Hierarchical design flow consists of following steps:
  - Draw design flow diagram
  - Create interconnect
  - Define memory map (if apply)
  - Define logic for leaf units
  - Define verification environment
  - Generate RTL, C++ and documentation

---
Processor design flow
Processor design flow consists of following steps:
  - Define ISA
  - Generate processor datapath components
  - Generate datapath control
  - Create interconnect
  - Create pipeline architecture
  - Create forwarding logic
  - Define memory map
  - Define verification environment
  - Generate RTL, C++ and documentation

---
CSL SOC design flow
SoC design flow consists of following steps:
  - Draw design block diagram
  - Select SOC bus type
  - Define SOC CSL memory map
  - Create CSL interconnect
  - Define logic for leaf units
  - Connect leaf units to SOC bus using hardware abstraction layer bus interface units
  - Define verification environment
  - Generate RTL, C++ and documentation

---
CSL Design Flow
user C++
simulator
code
documentation
HTML, PDF
csl
lib
.csl
pp
C++
generated
code
C++
compiler
cslc
csl pp
user
defined RTL
test bench
.csl
Verify
equivalence
RTL
test
bench
RTL
generated
code
RTL
simulator
Netlist
user RTL
defined
code
Bit stream
Synthesis
Place and
route
ASIC/RPGA

---
CSL a chip specification language (4)
ISA
(csl_isa_field,
csl_isa_element)
Hierarchy
(csl_unit,
csl_interface)
Interconnect
(csl_signal,
csl_port,
csl_signal_group)
Memory map
(csl_mem_page,
csl_mem_map)
IM
DM
IM
DM
Pn
P0
. . .
ALU
RF
SR
SEQ
Memory Bank0
Memory Bank m
. . .
DMA
Eth
MAC
GPI0
I2C
UART

---
CSL a chip specification language (4)
ISA
(csl_isa_field,
csl_isa_element)
Hierarchy
(csl_unit,
csl_interface)
Interconnect
(csl_signal,
csl_port,
csl_signal_group)
Memory map
(csl_mem_page,
csl_mem_map)
IM
DM
IM
DM
Pn
P0
. . .
ALU
RF
SR
SEQ
Memory Bank0
Memory Bank m
. . .
DMA
Eth
MAC
GPI0
I2C
UART

---
CSL a chip specification language (4)
ISA
(csl_isa_field,
csl_isa_element)
Hierarchy
(csl_unit,
csl_interface)
Interconnect
(csl_signal,
csl_port,
csl_signal_group)
Memory map
(csl_mem_map_page,
csl_mem_map)
IM
DM
IM
DM
Pn
P0
. . .
ALU
RF
SR
SEQ
Memory Bank0
Memory Bank m
. . .
DMA
Eth
MAC
GPI0
I2C
UART

---
CSL a chip specification language (4)
ISA
(csl_isa_field,
csl_isa_element)
Hierarchy
(csl_unit,
csl_interface)
Interconnect
(csl_signal,
csl_port,
csl_signal_group)
Memory map
(csl_mem_map_page,
csl_mem_map)
IM
DM
IM
DM
Pn
P0
. . .
ALU
RF
SR
SEQ
Memory Bank0
Memory Bank m
. . .
DMA
Eth
MAC
GPI0
I2C
UART