CSL ISA
Instruction set architecture

---
Instruction set architecture (ISA)
ISA descriptions are usually written by architects using text editors or spreadsheets.

---
Problems with hand written ISA descriptions
Instruction field positions and widths are drawn in figures.
Opcodes are added as separate tables.
Relationships between instruction formats are not clear and must be derived by the reader.

---
ISA tree of instruction formats
ISA's are described using a hierarchy of instruction formats. The hierarchy is effectively a tree of formats.
Parent instruction formats are inherited by the child instruction formats.
Child instruction formats add information to the parent instruction formats.

---
ISA instruction fields
ISA instruction fields can be added to each instruction format at each level of the instruction format tree.

---
ISA fields and enumerated types
ISA instruction formats have fields which can have an associated enumerated type.

---
ISA fields and enumeration items
ISA instruction parent formats which associate an enumerated type with a field which are inherited must use one of the enumeration items in the same field in a child instruction format.

---
ISA example
4.root_format
5.instr_format
1.csl_enum
7.instr_format
6.instr_format
3.csl_enum
2.csl_enum
9.instructions
8.instructions

---
ISA Example – csl code
//isa fields
//opcode field
csl_isa_field f_opcode {
  f_opcode () {
 set_type(opcode);
 set_width(2);
 set_enum(e_opcodes); }};
//conds field
csl_isa_field f_conds {
  f_conds () {
   set_type(subopcode);
   set_width(4);
   set_enum(e_conds); }};
//rconds field
csl_isa_field f_rconds {
  f_rconds () {
  set_type(subopcode);
  set_width(3);
  set_enum(e_rconds); }};
//enums
//1.opcodes enum
csl_enum e_opcodes {
    br=0
    // , call=1,
    // arithm=2,
    // load=3 };
//2.conds enum
csl_enum e_conds {
    // bpn=0,
    bpe=1,
    bple=2
    // , bpleu=3,
    // bpvc=15 };
//3.rconds enum
csl_enum e_rconds {
  brz=1,
    // brlez=2,
    // brlz=3,
    brgez=7 };

---
ISA Example – csl code
//rs1 field
csl_isa_field f_rs1 {
  f_rs1 () {
    set_type(address);
    set_width(7); }};
//rs2 field
csl_isa_field f_rs2 {
  f_rs2 () {
    set_type(address);
    set_width(9); }};
//op2 field
csl_isa_field f_op2 {
  f_op2 () {
    set_type(constant);
    set_width(1); }};
//imm field
csl_isa_field f_imm {
  f_imm () {
    set_type(constant);
    set_width(15); }};
//impl-dep field
csl_isa_field f_impl {
  f_impl () {
    set_type(constant);
    set_width(10); }};
//a field
csl_isa_field f_a {
  f_a () {
    set_type(constant);
    set_width(4); }};
//instruction formats
//4.root format
csl_isa_element root {
  root () {
    set_type(root_format);
    set_width(32); }};

---
ISA Example – csl code
//5.base format derived from root format
csl_isa_element base_format: root {
f_opcode f_opcode;
f_op2 f_op2;
base_format () {
set_type(instr_format);
set_position(f_opcode,30);
set_position(f_op2,15); }};
//6.format f1 derived from base format
csl_isa_element f1_format: base_format {
f_conds f_conds;
f_rs1 f_rs1;
f_imm f_imm;
f1_format () {
set_type(instr_format);
set_position(f_conds,25);
set_next(f_conds,f_rs1);
set_position(f_imm,0); }};
//7.format f2 derived from base format
csl_isa_element f2_format: base_format {
  f_rconds f_rconds;
  f_rs2 f_rs2;
  f_impl f_impl;
  f_a f_a;
  f2_format () {
      set_type(instr_format);
      set_position(f_rconds,27);
      set_next(f_rconds,f_rs2);
      set_position(f_impl,4);
      set_next(f_impl,f_a); }};
//instructions
//8.bpe instruction
csl_isa_element bpe_instr: f1_format {
  bpe_instr () {
       set_type(instr);
       f_opcode.set_enum_item(br);
       f_conds.set_enum_item(bpe); }};

---
ISA Example – csl code
//8.bple instruction
csl_isa_element bple_instr: f1_format {
bple_instr () {
set_type(instr);
f_opcode.set_enum_item(br);
f_conds.set_enum_item(bple); }};
//9.brz instruction
csl_isa_element brz_instr: f2_format {
brz_instr () {
set_type(instr);
f_opcode.set_enum_item(br);
f_rconds.set_enum_item(brz); }};
//9.brgez instruction
csl_isa_element brgez_instr: f2_format {
brgez_instr () {
set_type(instr);
f_opcode.set_enum_item(br);
f_rconds.set_enum_item(brgez);
}
};

---
Connecting signals to
instruction formats

---
Connecting signals to
instruction formats
An ISA object can be associated with a signal.
The ISA bit ranges in the signal can be accessed using the hierarchical identifier for the specific ISA field.

---
Generating assemblers automatically

---
Generating assemblers automatically (cont.)
Micro engines and small processors with custom instruction sets need software tools.
Assemblers can be generated for CSL ISA specifications.

---
Assembling code
The assembler can generate a binary executable which is loaded into a behavioral or structural memory model in the C++ simulator or RTL DUT.

---
Generated ISA component consumers
Who are the generated ISA component users?
Software tools team
Simulation team
RTL design team
Software drivers team
Software applications team

---
Software tools team
The software tools team uses instruction opcode constants and instruction field offsets to build assemblers and compilers.

---
C++ simulator team

---
RTL design team

---
Software driver team

---
Software applications team