CSL vectors
Connecting C++ simulators
and RTL testbenches

---
Vectors
Vectors are an ordered list of either DUT input or output ports and their associated values.

---
Vector types
Input vectors are applied to the DUT inputs and are called stimulus vectors.
Output vectors are compared to the DUT outputs and are called expected vectors.

---
CSL vector
Stimulus and expected vectors must have specified:
a unit, using the CSL command set_unit_name
a direction, using CSL command set_direction.

---
CSL vector
Each vector is associated to a unit
Vectors are used by the testbench, but are not instantiated in it.
The default checker type is cycle accurate.

---
Vector usage models
Vectors can be written to a file.
Vectors can be written to a socket.

---
Testbenches read vectors
Testbenches read vectors written from a file.
Testbenches read vectors from a socket.

---
Events
Events are defined so that we can indicate points at which to turn on and turn off the verification vector recording.
The verification vector is "captured" based on the verification vector type.

---
Events
Each time a verification vector event occurs the associated verification vector is recorded in a file.
The verification vector recording is turned on and off based on another set of events such as those corresponding to a reset or a unit enable

---
Cycle accurate vectors
Definition: Cycle accurate-Logic is modeled with the same number of pipestages in the C++ simulator and the vectors are captured captured each clock cycle.

---
Cycle accurate vectors
Example: If there are 5 pipe stages in the RTL design the C++ simulator will model the logic with a logic bubble corresponding to each pipe stage in the RTL.

---
Pipestage accurate vectors
Definition: Pipestage accurate-Logic is modeled with the same number of pipestages in the C++ simulator and the vectors are captured each clock cycle. However, the logic may be grouped into one or more pipestages and followed by all pipe stages.

---
Pipe stage accurate vectors
Example: If there are 5 pipe stages in the RTL design the C++ simulator can model the logic in one logic bubble and follow the logic bubble with 5 pipe stages. Where as the RTL design has a logic bubble corresponding to each pipe stage.

---
Transaction accurate vectors
Definition: Transaction accurate-Logic is modeled abstractly. All logic may be grouped into one or more pipestages and followed by a single pipe stage in the C++ simulator and the vectors are captured each on a valid transaction expression.

---
Transaction accurate vectors
Example: The RTL contains 5 pipe stages. The C++ simulator contains 1 pipestage.
Both contain a valid bit indicating that the pipe stage output contains a valid transaction. Vectors are captured when the valid bit is true. The valid bit can be a combination of signals.

---
Reset and vectors
Vectors are usually not captured prior to the assertion and de-assertion of reset.

---
Vector capture start and stop
A start event indicates when to start capturing vectors. Reset is a typical start event.
An end event indicates when to stop capturing vectors. End events include:maximum number of vectors captured,a complete video frame or a stream has been sent through the simulator.

---
Vector ID's
Vectors are associated with a unique vector ID.
The unique vector ID is written to the vector file.
The testbench will check that the vector file to read has the correct ID corresponding to the RTL ID and testbench ID.

---
Vector versions
Changing logic of a design causes associated vectors to change. Therefor vectors are associated with a vector version.
The vector version is written to the vector file.
The testbench will check that the vector file to read has the correct version corresponding to the RTL version and testbench version.

---
CSL_VECTOR example
Declaring the interface with ports
Declaring the unit and instantiate the interface
Associate the unit with the stimulus and expected vectors
Create the testbench that will use the created vectors

---
Declaring the interface with ports
csl_interface ifc {
csl_port stim_i(input,2), stim_o(input,2);
csl_port exp_i(output,2), exp_o(output,2);
ifc () {}
};

---
Declaring the unit and instantiate the interface
csl_unit dut {
csl_port clk(input);
ifc ifc_0;
dut () {
clk.set_attr(clock);
}
};

---
Associate the stimulus and expected vectors with the unit
csl_vector stim {
stim () {
set_unit_name(dut);
set_direction(input);
}
};
csl_vector exp {
exp () {
set_unit_name(dut);
set_direction(output);
}
};

---
Create the testbench that will use the vectors
csl_testbench tb {
csl_signal clk(reg);
dut dut_0;
tb () {
clk.set_attr(clock);
add_logic(clock,clk,100,ps);
}
};