CSL/CSLC
The Front End Chip Architecture, Design and Verification Productivity Solution

---
Part 2
CSL Language

---
Overview
CSL Language
CSL Unit
CSL Bitrange
CSL Field
CSL Enum
CSL Signal
CSL Signal Group
CSL Port
CSL Interface
CSL Expressions
CSL Assignment Statements

---
Overview
CSL Register
CSL Register File
CSL FIFO
CSL Pipeline
CSL Memory Map
CSL ISA
CSL Verification Components
CSL Testbench
CSL Prodcon
CSL Bus
CSL Bus Interface

---
CSL Language
CSL Language contains basic constructs of the language
  - constants
  - strings
  - tables
  - events
CSL Language also contains constructs that are used by more than one CSL tool:
    - enums
    - fields
    - lists
CSL Language defines the regular expressions that can be used with CSL
CSL Language defines the grammar of the CSL language

---
CSL Language
CSL language provides a rich set of objects and methods that can be used to specify a complex design
The set of CSL objects and their associated commands that a designer can use depends on the following:
  - type of the design
    - single or multi processor based
    - single cycle or pipelined
    - system on a chip
    - processing or control intensive
  - complexity of design
  - embedded functionality
  - available CSL component libraries

---
CSL Language
In order to use CSL at its best the user must have good knowledge in the following areas: architectural modelling, instruction set design, pipeline design, verification-testbench design
CSL is used for many different areas in the chip design process. Relationships exists between these areas which the designer must be aware of
Handling these relationships are eased (compared to other design tool packages) by the fact that all specifications are written using only one language

---
CSL Language
In the process of writing the specification of a design using CSL the designer must identify
  - hierarchies within different object groups: units, signals, instruction sets, memory maps, verification components
  - relationships between objects in the same group or in different group types
  - repeatability of different design patterns
These aspects can be captured in the CSL using specially intended language constructs
The compiler will check the validity of the specifications and if valid will preserve relationships guarding their consistency throughout all the design process

---
CSL Unit
Units are CSL language constructs that help organize logic into functional units blocks that can be:
  - instantiated
  - connected
  - added to other units in order to create hierarchies
A CSL unit can contain:
  - interfaces
  - signals
  - other CSL units
  - instances of CSL objects
Example of units: functional units, processors, FIFOs, register files. Though common design modules have separate CSL constructs, they are derived and inherit all proprieties and structures from the unit object

---
CSL Unit Example
In this example we demonstrate how units can be used to capture hierarchical relationship.
No interconnection and no functionality is specified for the units.
alu
mux21
osga
osgl

---
CSL Unit Example
CSL code
// define one stage arithmetic unit
csl_unit ostga { ostga(){}
};
// define one stage logic unit
csl_unit ostgl { ostgl(){}
};
// define a 2-to-1 multiplexer
csl_unit mux21 { mux21(){}
};
// module alu
csl_unit alu {
// add unit instances
ostga ostga0;
ostgl ostgl0;
mux21 mux21a;
alu() {}
};
Generated Verilog code
module ostga();
endmodule
module ostgl();
endmodule
module mux21();
endmodule
module alu();
ostga ostga0();
ostgl ostgl0();
mux21 mux21a();
endmodule

---
CSL Signal
Signals are CSL language constructs used to connect different design units and carry the information between current statements of the design
CSL signals are the equivalent of wires that connect different components of a system
CSL signals can be uni- or multidimensional
CSL signals are of different types and can have different attributes
CSL signal types are similar to Verilog signal types. Signal types are related closely to the hardware structure that is being described

---
CSL Signal Types

---
Signal attributes
Signal attributes are used to indicate special purpose signals
Signal attributes can be used by interconnect tool or autorouter in order to:
  - check signal compatibility
  - make special interconnects
  - allocate special hardware resources
  - generate specific hardware logic

---
Signal attributes

---
CSL Signal Example
csl_unit u {
// add signals
csl_signal s1(wire,4);
csl_signal s2(wire,8);
alu() { }
};

---
CSL Signal Group
Signals can be grouped together and assigned a symbolic name. Grouping signals is captured in CSL with the CSL Signal group construct.
We can connect tens of wires to tens of ports by defining a group of signals(a signal group in CSL) and a group of ports (an interface in CSL).
Connections of signal groups can be done manually (using the connect command or the the formal to actual connect feature of instantiation) or automatically by the autorouter.
In the first and third case, the connection will be made taken into account the order in which signals or ports have been added to the group or interface respectively.

---
CSL Signal Group
A signal group can include different types of signals. The signals can be uni or multidimensional
A signal group can include signals and other signal groups
A hierarchy of signals can be captured in CSL using signals and signal groups

---
CSL Signal Group Example
In this example we create three signal groups (yellow) of which two contain both signal (white) and signal groups.
s_data
sg_ma
sg_meb
32
s_addr
sg_rd_wr
24
64
s_rd
58
 2
s_wr
s_ctrl
6

---
CSL Signal/Signal Group Hierarchy
sg_meb
sg_ma
sg_rd_wr
s_data
s_addr
s_rd
s_wr
s_ctrl

---
CSL Signal Group Example
//CSL code
csl_signal_group sg_rd_wr {
csl_signal s_rd;
csl_signal s_wr;
sg_rd_wr () {} };
csl_signal_group sg_ma {
csl_signal s_data(32);
csl_signal s_addr(24);
sg_rd_wr sg_rd_wr_i;
sg_ma () {} };
csl_signal_group sg_meb {
csl_signal s_control(6);
sg_ma sg_ma_i;
sg_meb () {} };
csl_unit top {
sg_meb sg_meb_t;
top() {} };
// Generated Verilog code
module top();
wire [5:0] sg_meb_t_s_control;
wire [31:0] sg_meb_t_sg_ma_i_s_data;
wire [23:0] sg_meb_t_sg_ma_i_s_addr;
wire sg_meb_t_sg_ma_i_sg_rd_wr_i_s_rd;
wire sg_meb_t_sg_ma_i_sg_rd_wr_i_s_wr;
endmodule

---
CSL Signal Group
Signal groups can be used by the autorouter to make group of signals “traverse” unit scopes boundaries
After traversal, the grouped set of signals can remain grouped and connected to an appropriate interface (cslc checks the consistency of connection) or can be split into individual signals or lower level signal groups to be connected to lower level interfaces or individual ports

---
CSL Port
CSL ports are CSL language constructs that specify the interface through which units communicates with other units in the same design space
CSL ports can have different direction types :
  - input
  - output
  - bidirectional
CSL ports can have same types as defined for signals
CSL ports can be used in conjunction with CSL interfaces in order to create reusable and hierarchical interfaces for units in a design

---
CSL Port
CSL ports are specified by direction, type and range.
Ports can be created by copying proprieties from other already defined ports and direction can be switched in order to create unit interfaces that can be connected together
CSL specifications that include ports declarations are checked for valid connections, compatible types and attributes
Consistency of CSL ports declaration is also checked by the autorouter in its attempt to make correct and optimum connections between design units

---
CSL Port Example
In this example we demonstrate how to define units ports
We define 2 units, each has two ports, the directions and bitranges allow the connection of the two units
7
        p_a
u_a
        p_b
p_a
u_a
        p_b
3

---
CSL Port Example
//Generated Verilog code
module u_a(p_a,
p_b);
input [7:0] p_a;
output reg [3:0] p_b;
endmodule
module u_b(p_a,
p_b);
input [3:0] p_b;
output reg [7:0] p_a;
endmodule
//CSL code
csl_unit u_a {
csl_port p_a(input,wire,0,7);
csl_port p_b(output,reg,0,3);
u_a(){
}
};
csl_unit u_b {
csl_port p_a(output,reg,0,7);
csl_port p_b(input,wire,0,3);
u_b() {
}
};

---
CSL Interface
Interfaces are containers for the port list of a unit
Instances of interfaces can be used in units that have same signal sets.
More than one interface of the same or different type may be added to one unit.
A unit can contain instances of the same or of different interfaces.

---
CSL Interface
Modifying the contents (adding, deleting or changing the port names) of the interface container modifies the contents of all instances of the interface.
The port directions of all signals in an instance of an interface may be reversed using the reverse() method
There are not reversed signals connected to the port which have a dont_modify_direction attribute.

---
CSL Interface and Signal Group Example
In this example we create three signal groups (yellow) of which two contain both signal (white) and signal groups.
s_data
32
sg_ma
64
sg_meb
s_addr
24
s_rd
sg_rd_wr
 2
58
s_wr
6
s_ctrl

---
CSL Interface and Signal Group Hierarchies
ifc_me
sg_meb
ifc_ma
sg_ma
ifc_rd_wr
sg_rd_wr
data
addr
rd
wr
ctrls
data
addr
rd
wr
ctrls

---
CSL Interface and Signal Group Example
//CSL code
// Generated Verilog code
module meng(ifc_me_i_ifc_me_ma_i_ifc_rd_wr_i_wr,
ifc_me_i_ifc_me_ma_i_ifc_rd_wr_i_rd,
ifc_me_i_ifc_me_ma_i_data,
ifc_me_i_ifc_me_ma_i_addr,
ifc_me_i_ctlrs);
output reg ifc_me_i_ifc_me_ma_i_ifc_rd_wr_i_wr;
output reg ifc_me_i_ifc_me_ma_i_ifc_rd_wr_i_rd;
output reg [24:0] ifc_me_i_ifc_me_ma_i_addr;
output reg [5:0] ifc_me_i_ctlrs;
inout [32:0] ifc_me_i_ifc_me_ma_i_data;
endmodule
module topunit();
wire [5:0] sg_meb_i_ctlrs;
wire [31:0] sg_meb_i_sg_ma_i_data;
wire [23:0] sg_meb_i_sg_ma_i_addr;
wire sg_meb_i_sg_ma_i_sg_rd_wr_i_rd;
wire sg_meb_i_sg_ma_i_sg_rd_wr_i_wr;
meng meng1(.ifc_me_i_ctlrs(sg_meb_i_ctlrs));
endmodule

---
CSL Interface and Signal Group Example
// Generated Verilog code
module meng(ifc_me_i_ifc_me_ma_i_ifc_rd_wr_i_wr,
ifc_me_i_ifc_me_ma_i_ifc_rd_wr_i_rd,
ifc_me_i_ifc_me_ma_i_data,
ifc_me_i_ifc_me_ma_i_addr,
ifc_me_i_ctlrs);
output reg ifc_me_i_ifc_me_ma_i_ifc_rd_wr_i_wr;
output reg ifc_me_i_ifc_me_ma_i_ifc_rd_wr_i_rd;
output reg [24:0] ifc_me_i_ifc_me_ma_i_addr;
output reg [5:0] ifc_me_i_ctlrs;
inout [32:0] ifc_me_i_ifc_me_ma_i_data;
endmodule
module topunit();
wire [5:0] sg_meb_i_ctlrs;
wire [31:0] sg_meb_i_sg_ma_i_data;
wire [23:0] sg_meb_i_sg_ma_i_addr;
wire sg_meb_i_sg_ma_i_sg_rd_wr_i_rd;
wire sg_meb_i_sg_ma_i_sg_rd_wr_i_wr;
meng meng1(.ifc_me_i_ctlrs(sg_meb_i_ctlrs));
endmodule

---
CSL Interface Example
csl_unit u2{
  - ifc ifc2l, ifc2r;
  - u2(){
    - ifc2l.reverse();
    - ifc2r.reverse();
  - }
};
csl_unit u3{
  - ifc ifc3l, ifc3r;
  - u3 (){}
};
u[[1-3]].ifc[\1].reverse();
u[[1-3]].ifcu[\1]r.connect(u[[2-3]|{1}]).ifc[\2]l;
csl_interface ifc{
  - csl_port a(input);
  - csl_port b(input);
  - csl_port c(output);
  - ifc () {}
};
csl_unit u1{
  - ifc ifc1l, ifc1r;
  - u1(){
    - ifc1l.reverse();
    - ifc1r.reverse();
  - }
};

---
CSL Interface
csl_interface ifc{
  - csl_port a(input), b(input);
  - csl_port c(output);};
csl_unit unit{
  - ifc ifcl,ifcr;
  - unit(){
    - ifcl.reverse();
  - } };
csl_unit top{
  - unit u0, u1, u2;
  - top(){
  - u[[0-2]].ifcu[\1]r.connect(u[[1-2]|{0}]).ifc[\2]l;
  - }
};
u2
u3
u1
x
y
z
x
y
z
x
y
z
x
y
z
x
y
z
x
y
z
ifc1l
ifc1r
ifc2r
ifc3r
ifc2l
ifc3l

---
CSL Bitrange
CSL language construct that specifies ranges for bit aggregate objects. CSL bitrange extends common definition of bitrange in the sense that it is a named bitrange. Thus, it can be reused to specify bitranges for signals, ports, fields, and vectors.
Using CSL bitranges the user has an easy way to specify multidimensional signals and ports
There are available different range declaration types specifying:
  - lower_limit, upper_limit
  - width (implicitly lower_limit=0)
The bitrange width can be a constant or numeric expression

---
CSL Bitrange
In CSL concatenation of bitranges is possible
Relation to other bitranges can be specified using offset
There are available functions to get parameters of a bitrange from another bitrange in order to set the parameters of a new created bitrange to be in relationship with the initial ones

---
CSL Bitrange Example
In this example we demonstrate how to use bitranges in defining units ports
We define 2 units, each has two ports, the directions and bitranges allow the connection of the two units. Dimension of ports are specified using the CSL bitrange construct. If bitrange modifies, we need to change code only in one place.
7
        p_a
u_a
        p_b
p_a
u_a
        p_b
3

---
CSL Bitrange Example
//CSL code
csl_bitrange brd(0,7);
csl_bitrange brs(0,3);
csl_unit u_a {
csl_port p_a(input,wire,brd);
csl_port p_b(output,reg,brs);
u_a(){
}
};
csl_unit u_b {
csl_port p_a(output,reg,brd);
csl_port p_b(input,wire,brs);
u_b() {
}
};
//Generated Verilog code
module u_a(p_a,
p_b);
input [7:0] p_a;
output reg [3:0] p_b;
endmodule
module u_b(p_a,
p_b);
input [3:0] p_b;
output reg [7:0] p_a;
endmodule

---
Specifying offset
// CSL code
csl_unit _2bit_flip_flop{
csl_port p_data(input),clk(input),enable(input),q(output);
_2bit_flip_flop() {
p_data.set_width(2); } };
csl_unit ff_a {
csl_port p_data_a(input),clk_a(input),enable_a(input),q_a(output);
ff_a () { set_offset(2); } };
csl_unit ff_b {
csl_port p_data_b(input),clk_b(input),enable_b(input),q_b(output);
ff_b () { set_offset(2); } };
csl_unit ff_c {
csl_port p_data_c(input),clk_c(input),enable_c(input),q_c(output);
ff_c() { set_offset(4); } };
csl_unit decoder {
csl_port dec_in(input,6), dec_out(output,64);
decoder () { add_logic(gen_decoder); } };
_2bit_flip_flop ff_[[a-c]](.p_data(in_[\1]),
.enable(enable), .clk(clk_[\1]),.q(out_[\1])));
csl_list(ff_[[a-c]].in_[\1]).connect(dcd.d_in);

---
Specifying offset
enable
flip_flop_a
2
2
in_a
clk_a
out_a
[0:1]
flip_flop_b
6
2
2
64
decoder
in_b
[0:1]
[2:3]
clk_b
dec_in
out_b
[0:5]
flip_flop_c
2
2
in_c
clk_c
[4:5]
out_c
[0:1]

---
CSL enumerated type (enums)
CSL Enum is an abstract data type that takes values in a finite set of identifiers
CSL Enum is used for variables that do not have any numerical order
CSL Enum is used for defining
  - types
  - identifiers
  - naming conventions
  - attributes
  - mnemonics
  - aliases

---
CSL Enums
Enums may be attached to signals, fields, and registers.

---
CSL_ENUM Examples
csl_enum packet_type{green, blue, red};
csl_enum prefix_type{NO_PREFIX, PIPELINE_NAME, PIPESTAGE_NAME, PIPELINE_PIPESTAGE_NAME};

---
CSL Field
Fields are bit ranges that are named objects.
Fields have an upper and a lower bit range index.
Fields can be grouped to form greater fields and multibit filelds can be split in smaller fields. These operations generate a hierarchy that can be used in the design specification of instruction sets.
Fields may be joined with other fields using a linked list like set_next or set_previous operation.
Enums can be associated with fields. CSLC checks that the enum size accomodate with the size of the field bitrange.

---
CSL Field
All commands that apply to bitrange, apply also to csl_field without the multidimensional commands
When associated with an instruction from an ISA, it can be used to generate control signals decoded from the fields of the instruction register

---
CSL Field Example
csl_enum e{
ADD,
SUB
};
csl_field fd{
fd(){
set_width(4);
set_enum( e);
}
};

---
CSL List
CSL List is a language construct that allows the user to specify a list of objects and use it as a single object
CSL lists must contain object of the same type
CSL lists are defined by user or can be generated by the regular expression preprocessor from regular expressions in the specification
CSL list can be used in foreach statements

---
CSL List Example
Example 1. Create the list of signals a and b and set the same bitrange to these signals using the defined list:
csl_bitrange br_br(7,0);
csl_unit u_chip{
  - csl_signal a(wire),b(wire);
  - csl_list lista (a,b);
  - chip(){
    - lista.set_bitrange(br_br);
  - }
};

---
CSL List Example
Example 2. Set enum to fields in the instruction format from an instruction set (ISA)
csl_enum e_enum{BNZ,BEQ,BZ};
csl_isa_field field(5);
field.set_type(opcode);
csl_isa_element if_format{
  - field f_opcode, f_srca, f_srcb, f_dest, cond1,cond2;
  - csl_list f_list (cond1, cond2);
  - if_format(){
    - set_type(root_format);
    - f_list.set_enum(e_enum);
  - }
};

---
CSL Regular Expressions
CSL language supports regular expressions (regex)
Regular expressions cause CSL declarations and reference statements to expand into multiple statements
There are two main types of regular expressions
  - generate expressions
  - search expressions

---
CSL Regular Expressions Examples
//CSL code
for (int i=0; i<3; i++){
string col = “col_” + i + “_” + ”[[0-3]]”;
csl_signal col[13:0];
}
//generated Verilog code
wire col_0_0[13:0]
wire col_0_1[13:0]
wire col_0_2[13:0]
wire col_0_3[13:0]
wire col_1_0[13:0]
wire col_1_1[13:0]
wire col_1_2[13:0]
wire col_1_3[13:0]
wire col_2_0[13:0]
wire col_2_1[13:0]
wire col_2_2[13:0]
wire col_3_3[13:0]
wire col_3_0[13:0]
wire col_3_1[13:0]
wire col_3_2[13:0]
wire col_3_3[13:0]

---
Regular expressions