CSL/CSLC
The Front End Chip Architecture, Design and Verification Productivity Solution

---
Outline
Overview
Tools
Syntax
Design Examples

---
Part 4
CSL/CSLC
Design Examples

---
Design example
The design flow will consist of the following steps:
draw the chip block diagram
create hierarchy
create interfaces for modules
connect special signals (clock, set/reset)
make connections between modules

---
Design example
define instruction set architecture
define memory map
generate library components to be instantiated in the modules
write logic for each unit and include in a leaf level unit generated from the interconnect
generate testbench and verification components for chip verification
write C++ model for the chip
simulate the design and compare RTL model outputs with C++ model outputs

---
Design example. Block diagram
chip
alu
im
rf
pc
id

---
Design example: Defining memory map
//a memory_map_page with an address range from 0 to 47 with an increment 1 and set the memory word width to 32-bits
csl_memory_map_page chip_mem_map_pg{
chip_mem_map_pg(){
add_address_range(0,47);
set_address_increment(1);
}};
csl_memory_map chip_mem_map{
chip_mem_map(){
set_type(hierarchical);
set_data_word_width(32);
}
};

---
Design example. Defining hierarchy
chip
pc
alu
rf
im
id

---
Defining hierarchy. CSL code
// CSL code
csl_unit pc {
pc () {} };
csl_unit im {
im () {} };
csl_unit id {
id () {} };
csl_unit rf {
rf () {} };
csl_unit alu {
alu () {} };
csl_unit chip {
pc pc0;
im im0;
id id0;
rf rf0;
alu alu0;
chip () {}
};
// Verilog code
module pc();
endmodule
module im();
endmodule
module id();
endmodule
module rf();
endmodule
module alu();
endmodule
module chip();
pc pc0( );
im im0( );
id id0( );
rf rf0( );
alu alu0( );
endmodule

---
Design example. Adding interfaces
chip
pc
alu
rf
im
id

---
Design example. Adding special signals
chip
pc
alu
rf
im
id
clk/reset

---
Design example: Connect modules

---
Design example: Define ISA

---
Design example: Program counter
chip
pc
alu
rf
im
id
pc_0
pcr
clk/reset

---
Design example: Instruction memory
chip
pc
im
alu
rf
id
pc_0
im_1
instr_
mem
pcr
clk/reset

---
Design example: Instruction decoder
chip
pc
im
alu
rf
id
pc_0
im_1
instr_
mem
pcr
dec
clk/reset

---
Design example: Register file
chip
pc
im
alu
rf
id
pc_0
im_1
instr_
mem
pcr
dec
clk/reset
   rf
32x32

---
Design example: ALU
chip
pc
im
alu
rf
id
pc_0
im_1
+/-
instr_
mem
pcr
dec
O
<<
>>
clk/reset
   rf
32x32

---
Design example: Write logic

---
Design example. Generate testbench and verification components

---
Design example. Write C++ model

---
Design example. Simulate the design