# Fastpath Logic, Inc. Whitepaper
Why build when you can buy?
Abstract:
Fastpath Logic has built a new type of tool (CSLc) that generates chip infrastructure and verification support C++ code and RTL code, and documentation from a single input. A single language is used to describe chip infrastructure and verification support structures. Relationships between these structures results in a synergy that cannot be achieved using multiple point-tools. A single language compiler can check the relationships between the parts of the chip infrastructure and verification support description. Multiple point tools cannot check the relationships between multiple chip infrastructure and verification support descriptions. In addition CSLc can check the connections between Verilog RTL and the chip and verification intrastructure. CSLc is a single point tool which results in a more efficient design process. It is currently estimated that design teams spend 50% of their time verifying chips. Many of the bugs that need to be fixed are consistency bugs between design elements and between the design, the simulator and or verification environment. CSLc prevents these types of bugs by using a single input to specify the and the chip and verification intrastructure components and the connections between these components.

CSL parameterizable libraries will be available to support the following development activities:
- generation of code for system on chip buses in software tools, C++ simulators and RTL models. Each unit in the design is connected to a bus interface (abstraction layer) which can be connected to different SoC buses.
- hierarchical MBIST generation. A centralized controller, and executin units can be generated with the associated firmware tests in C++ and RTL.
- test unit generation. a test unit for controlling on chip testing

Maintaining a consistent design/model/software is difficult. Why spend resources developing and maintaining an in-house tool suite when FPL has a professionally maintained and documented tool that solves all your chip-infrastructure needs. Why use point tools from a variety of vendors when FPL has all you’ll need and more. Why build when you can buy.?