# Fastpath Logic, Inc. Whitepaper
Automating the generation of cycle based C++ simulators, C++ vector and state data writers and readers, and test benches.
Abstract:
Fastpath Logic has built a new type of tool (CSLc) that generates chip infrastructure and verification support C++ code and RTL code, and documentation from a single input. A single language is used to describe chip infrastructure and verification support structures and relationships between these structures results in a synergy that cannot be achieved using multiple point-tools. A single tool can check and create the connections between the C++ simulator units and vector writers and readers. It can also check and create the connections between the
 . In addition CSLc can check the connections between Verilog RTL and the chip and verification intrastructure. CSLc is a single point tool which results in a more efficient design process. It is currently estimated that design teams spend 50% of their time verifying chips. Many of the bugs that need to be fixed are consistency bugs between design elements and between the design, the simulator and or verification environment. CSLc prevents these types of bugs by using a single input to specify the and the chip and verification intrastructure components and the connections between these components.
The logic in the DUT is tested using a C++ simulator or some other source creates the stimulus and expect vectors. The stimulus vectors drive the DUT. In response the DUT produces output transactions. The DUT output transactions are compared against the expected vector transactions for correctness.
There is an entire generation of verification engineers who have learned how to write cycle based C++ simulators. The engineers write C++ code which is evaluated only once per clock cycle. The cycle based C++ simulators use libraries to implement the simulation engine. The simulator engineers can model the connections (e.g. wires and ports) using C++ scalars (e.g. unsigned int's) and aggregate structures (e.g. structures, classes, STL vectors, etc.) . Thes simulator engineers use C++ constants and functions generated by code generators in the cycle based C++ simulators. The C++ constants and functions are equivalent to RTL constants (e.g. 'defines, paramters, bit ranges, part selects) and RTL code (e.g. Verilog module interfaces, always blocks implmenting registers, etc.) generated by code generators.

The goal of a chip's simulation and verification teams is as follws:
1. Run sysetm level use cases to verify the functionality of the design (e.g. simulate a graphics pipeline and generate pictures) to verify that the algorithms are correct
2. Generate stimulus vectors to drive the inputs of the design under test in a test bench.
3. Generate expected vectors to compare against output of the design under test in a test bench.
4. Generate expected state data memory images to compare against the memory instances in the design under test in a test bench.
5. Model the cycle accurate behavior of the algorithm where necessary.
6. Create “golden” output (e.g. graphics framebuffers, encoder currenct and reference frames) to range check (e.g. the precision of the two models may differe) compare against the RTL DUT output.
7. Create vector extraction points at the system (in a multi-chip or SOC environment), chip or core level, and finally the block level.
The output of the simulator is either written to files or to a socket. The testbench reads the simulators generated output from either a file or socket, applies the stimulus vectors to the inputs of the design under test, and compares the outputs of the design under test to the expected vectors and compares the DUT's internal state data to the expected state data. Alternatively the stimulator can act as the test bench using socket PLI's and the simulator can “plug in” the DUT in as a replacement for a simulator module using a simple testbench to connect the DUT to the simulator. The simulator and DUT are then run concurrently using co-simulation. Additional verification techniques such as bubble injection into the stimulus vectors and random stalls applied to the design under test can be incorporated into the test bench to find temporal bugs. The same signals with the same widths, and in the same order must be used in all vectors and module interfaces. The C++ simulator vector signal order and signal widths must match the the size of the test bench memory if the vector file is loaded into a memory. The outputs of the memory must be connected to a set of signals which match the vector loaded into the memory. The set of memory output signals must match the set of ports in the module's input interface. In the case of output vector comparison the same set of rules apply except the memory contains expected vectors and the memory outputs are compared to the design under test. The expected vector memory is connected to a comparator and the DUT output vector is connected to the same comparator. The C++ simulator variable widths (e.g. a mask is used to extract the correct bit values from the C++ variable) and the order of the variables in the vector and the signals in the test bench which are connected to memories, module ports, and comparators need to be the same size as the signals in the vectors and must be connected to each memory in the correct order. Otherwise simulation mismatches will occur due to signal width and signal ordering inconsistencies in the C++ vectors and RTL signals in the test bench and module ports. A single tool can automatically generate the C++ code which generates the vectors with the same signal widths and signal order as the test bench memory or socket PLI. A single tool can automatically generate the RTL module and module interface, A single tool can automatically generate the RTL test bench code which contains the signals connected to the test bench memory, the comparator and finally the module's interface. A mismatch in any one of the following connection points will result in a simulation faliure:
- The C++ simulator and the output vector
- The C++ simulator vector and the test bench memory
- The test bench vector memory and the test bench memory output signals connected to the memory
- The stimulus vector memory output signals and the inputs to the design under test
- The expected vector memory output signals and the inputs to the comparator
- The outputs of the design under test and the inputs to the comparator
Moreover, the signals and events which control the vector and state data generation and comparisons must be controlled by the correct signals. The following is a list of signals which control the vector and state data generation and comparison.
- The C++ simulator start vector generation signal
- The C++ simulator stop vector generation signal
- The C++ simulator event capture event
- The C++ simulator reset signal
- The C++ simulator clock signal
- The test bench start vector compare signal
- The test bench stop vector compare signal
- The test bench event compare event
- The test bench reset signal
- The test bench clock signal
- C++ simulator golden model and the DUT golden model comparison signal
The verification of chip designs using C++ simulators is an accepted industry practice on processor and multimedia chip projects. CSLc generates the skeleton of a cycle based C++ simulator solution which is tied to the test bench and which is used to verify the RTL design under test. The two models are connected via a test bench. There are many points in the connections between the two models where bugs can be introduced which are not related to bugs in the design.

The example in the figure “interface consistency” shows the CSLc generating components in a cycle based C++ simulator and an RTL test bench. In the figure the different itnerfaces are shown that have to be created to capture the stimulus and expected vectors and state data from the C++ simulator when ever a capture event occurs. The stimulus vectors are loaded into a memory which is then drives the DUT. The Dut state data and output vectors are compared against the expected state data and vectors respectively when ever a compare transaction occurs in the DUT. The golden images are written by the test bench to a file which is compared to the golden file generated by the C++ simulator either by the testbench, which may slow down the simulation, or by a post processing script after the simulation finishes.

Using a single source that CSLc automates the creation and maintainance of the C++ simulator, test bench and RTL compenents involved in the verification of the DUT. The above example is one example of the automation facilities that CSLc provides.

SystemC event driven simulation is slower than cycle based simulation.
the users current testbench -Cadence e, Vera, System-C - and how CSLc compliments their existing or prefered solution.

One testbench will not meet all the verification requirements of a project team.

The following figure “interface consistency” shows just one aspect of the C++ simulator, verification infrastructure (the testbench), and the design that can be automated using a single input and a design automation tool. The single input file (.csl) and possibly CSL library files are compiled. The compiler generates the C++ simulator design hierarchy which may or may not be as detailed as the RTL implementation hierarchy. Moreover, the two hierarchies are guarenteed to match at certain levels specified by the user in the single input. Vector capture units in the C++ simulator create files (in the future socket connections will be supported). CSLc creates a test bench which contains memories which the vector files will be loaded into. Additional code to support loading the files into the test bench memories is generated. The memories are automatically connected to the test bench inputs and comparator outputs. The design interface is generated automatically and matches the generated signals in the test bench. Each time a signal name, signal width or vector changes the C++ and RTL verification and chip infrastructure files are updated automatically. All members of the simulation, design, software tools, and RTL design teams receive the updated changes