TEST PLAN
Enum: enum item with:
valid	- verilog numbers / - operation with verilog/simple numbers / ( operations = +, -, /,* etc) / - use it in an unit : - signal = enum (check the verilog output)
invalid	- invalid verilog numbers / - float numbers / - valid/ invalid operation with valid/ invalid verilog/ simple numbers / - valid/ invalid operations with float numbers
assign to	AO

Bitrange:
valid	- verilog/ simple numbers / - operation with verilog/simple numbers / ( operations = +, -, /,* etc) / - use it in a unit: - port (check the verilog output)
invalid	- invalid verilog numbers (width/ lower/upper) / - float numbers (width/ lower/upper) / - valid/ invalid operation with valid/ invalid verilog/ simple numbers(width/ lower/upper) / - valid/ invalid operations with float numbers
assign to	AO

Field:
valid	- create hierarchical fields / - add instances of the same field to different fields / - add multiple instances of the same field / - add a field using set_field_position with a position that is in bounds / - add fields using the 3 variants: / - explicit using set_field_position / - implicit using set_next and set previous / - implicit by instantiation / - position fields using 1 from the 3 variants / - position fields using combination of 2 from the 3 variants / - position fields using combination of the 3 variants / - add fields using different adding orders / - from left to right / - from right to left / - from center to sides / - from sides to center / - random / - insert fields between other two fields using set_next, set_previous / - create hierarchical fields with: / - all bits in fields / - unused bits / - reserved bits
invalid	- add a field using set_field_position with a position that is completely beyond the lower or the upper bound / - add a set_field_position with a position that is overlapping upper or lower bound / - add a field using set_next and set_right without a reference field / - add a field with set_next and set_right with reference to itself / - add a field with parent as reference / - add a field to itself / - add a field / - add a parent field to a child field (cycle)
assign to	PE

Register:
valid	- use as it was intended(see the docs): instantiate it into a testbench or unit and make it count something / - use legal values for start/end/reset/stop... / - create a register with default parameters / - create a register with one additional port / - create a register with 2, 3, 4... additional ports
invalid	- for each command specific to the counter registers being called by a register of type register / - for each command specific to a counter registers being called by a register without a type set - for each command with wrong/invalid/more/less arguments - test with start value bigger than end/stop value / - and more than one of the same special port (reset, set, init, clear) / - set counter width less than needed to reach stop/end value / - set counter start value greater than maximum count possibility / - set count amount greater than maximum count possibility
assign to

Vector: test with:
valid	-stimulus and expected vectors for a DUT (the DUT has to have input and output ports/interfaces) / - DUT has simple ports / - DUT has different interfaces for input and output ports / - DUT has interfaces with mixed input and output ports / - DUT has interfaces and simple ports / - exclude/include_only simple ports / - exclude/include_only some ports from interfaces / - exclude/include_only some interfaces
invalid	- missing stimulus and expected vector - missing stimulus vector for a DUT - missing expected vector for a DUT - stimulus and expected vectors but no ports/interfaces in the DUT - 1 or more inout ports in the DUT - 1 or more inout ports in an interface from the DUT - include a port that does not exist/is from another unit - exclude a port that does not exist/id from another unit / - exclude all ports from DUT - set the direction to input then exclude/include an output port - set the direction to output and include/exclude an input port - include clock/reset ports - make tests for each command with wrong/more/less arguments / - set vc_capture_ edge_type both rise and fall / - set output_filename illegal values
assign to

Testbench: unit with:
valid	- clock, tb with clock and add_logic(clock, ...) / - use all of the testbench options when possible, not just setting a clock and bob's your uncle / - instantiate a unit all types of compatible csl classes into a testbench, not just an unit
invalid	- clock, tb without clock but with add_logic(clock, ...) - clock, tb without clock and without add_logic(clock, ..) - clock, tb with clock and with add_logic(clock, ...) - clock, tb with clock but without add_logic(clock, ..) - clock, tb without clock and without add_logic(clock, ..) / - instantiate incompatible csl classes. / - set the clock to a multibit signal. - make multiple testbenches and multiple vectors of different types
assign to

MemoryMap:
Test add_address_range and add_reserved_address_range with add method(legal and illegal):
valid	- add all addressable objects on valid address (exists and not reserved) (add reserved addresses also) - add multiple objects on valid addresses with reserved and invalid address ranges between them
invalid	- add an address range with illegal values for upper and lower - add an reserved address range on an illegal range - add an reserved address range that overlaps with an illegal range(on lower and upper) - add an reserved address range on a valid but not free range - add an reserved address range that overlaps with a valid but not free range - add all addressable object to reserved addresses - add all addressable objects to illegal addresses(outside of every range) - add all addressable objects to addresses not free(address is already assigned to an object) - add all addressable objects to address ranges smaller than the depth of the object. - add multiple addressable objects with the sum of the depths bigger the the depth of the sum of the valid address ranges available.
assign to	IC

Test commands that change the increment value or change the next address(set_data_word_width, set_alignement, set_address_increment, set_next_address):
valid	- add multiple objects with objects depth smaller than the increment - add multiple objects with objects depth bigger than the increment(should allocate more address space than the increment) - add multiple objects with increment bigger and smaller than the increment - set the next address to the end+1 of a reserved address range and add objects - set the next address to the end+1 of a illegal address range - set the next address at the end+1 of a not free address range - set the next address bigger than the increment+current address - set the next address smaller than the increment+current address(but on a free address range) - set the next address on a bigger value than the increment+current address and then go back a few addresses with set_next and try to add objects(but on a free and not reserved address) - set the next address to a valid address and add an object with bigger depth than the remaining address range until the next illegal /reserved/not free address range(but there is a free, not reserved and legal address range to fit the object after that address)
invalid	- increment value goes over the current address range end and add objects - increment value bigger than the address range - increment value set by data_word_with and alignment bigger than the address_range - current address+increment goes on a reserved address - current address+increment goes on a illegal address(but not bigger than the upper bound of the page) - increment does not divide exactly to the no of addresses and add objects to fill the page and try to add one more - set the next address to a illegal address - set the next address to a reserved address - set the next address to a not free address - set the next address to a valid address and add an object with bigger depth than the remaining valid address range(test with reserved, illegal and not free address ranges)
assign to

set_symbol_max_length:
valid	- set the symbol max length and add objects with lower or equal symbol length - set the symbol max length and use get function to set it for other pages and add object to all pages
invalid	- set the symbol max length and add objects with symbols bigger than the max length - set the symbol max length and use get function to set it for other pages and add objects with bigger symbols to the pages that have the symbol max length set with the get function
assign to

set_type for memory map:
valid	- for the legal tests above create tests with a hierarchical, virtual with page no in address, virtual with base address and flat memory maps
invalid	- creates tests with hierarchical pages and set the type to a flat/virtual(both) mem map - creates tests with multiple pages but not hierarchical and set the type to a flat mem map
assign to

set_access_rights and set_access_rights_enum:
valid
invalid
assign to	IC

set_prefix and set_suffix
valid	- for all the above tests set the prefix and suffix to all pages and mem maps with legal values
invalid	- empty prefix - empty suffix - prefix and suffix having illegal params (not strings) - prefix that have a string param that starts with a illegal identifier char(number, *, etc.) - prefix and suffix that have a string param that contains a illegal identifier char(*, -, +, etc.) - prefix and suffix that have string params that contain '.'
assign to

Memory:
valid	- create memory with different widths/depths / - initialize memory with different valid values
invalid	- initialize memory with a value or seed_value greater than the number that can be represented on width bits / - invalid values for set_width and set_depth
assign to

Register file:
valid	- make all types of registers there are - instantiate them into units, testbench alongside other components - set the type of the register then set specific commands for it according to it's type (only register and counter available for now). - instantiate fields and isa fields in register scope.
invalid	- instantiate registers where they're not supposed to be, add signals or signal groups there, and so on / - make everything backwards
assign to

Verification Components:
valid	- even if you cannot declare a vector with only set_module_name and set_direction, use the verification components commands for it in different combinations. - take care that the unit you associate with the vector through "set_module_name" has ports (inputs and/or outputs) or interfaces with ports in them. - set_direction to the vector accordingly to what you want it to be (stim or expect), and use the exclusion_list and include_only to fine tune the ports(in or out) or interfaces that you want to work with from the associated unit.
invalid	- setting a module name to a non existing unit is the simplest thing anyone can do. - try to exclude/include ports/interfaces that are not in the associated unit. - try to include input ports to an expected vector and the other way around (outputs to stim).
assign to

Isa:
valid	- different tree structures of isa_elements / - create a structure where format has only instructions as children / - create structure where format has instructions and formats as children / - position fields in formats starting from – left, right, center / - associate enum to isa_field / - set fields in isa_element(formats) using the 3 possibilities (variants): / - explicit using set_position / - implicit using set_next and set previous / - implicit by instantiation / - position fields using 1 from the 3 variants / - position fields using combination of 2 from the 3 variants / - position fields using combination of the 3 variants / - set_enum_item in formats / - set_enum_item in instructions / - create formats with: / - all bits in fields / - unused bits / - reserved bits / - 1 opcode / - 1 opcode and 1 subopcode / - 1 opcode and 2 or more subopcodes / - create formats for all types of instructions: / - operations( arithmetic, logic...) / - load/ store in registers / - load/ store in memory with different addressing mechanisms / - branch / - conditional branch / - support for subroutines / - hardware interrupts / - test bits / - shift / - no operations
invalid	- add an isa_field using set_field_position with a position that is completely beyond the lower or the upper bound of format / - add a set_isa_field_position with a position that is overlapping upper or lower bound of format / - add an isa_field using set_next and set_right without a reference isa_field / - add an isa_field with set_next and set_right with reference to itself / - associate different enums to the same isa_field / - set an enum_item to an isa_field that has already set an enum_item / - set an enum_item to an isa_field from an enum different that the one already set / - set an enum that has more elements than can be represented on field bits / - set an enum that has values for enum_items bigger than can be represented on field bits
assign to

Fifo:
valid	- create csl units of type fifo (use the only two legal and mandatory commands / available: set_width, set_depth) – check the verilog code(check that all necessary signals are generated and that they have the correct widths) / - instantiate fifo units in other units and in testbenches(check the generated verilog codes) / - formal to actual mapping between a fifo instance and another unit(check if the default port names are correctly generated and available for the user)
invalid	- declare user defined ports and signals inside the scope of a fifo / - declare a fifo unit without specifying the width and depth / - declare a fifo without specifying the width or depth / - code a formal to actual mapping and include inexistent fifo ports (that were not generated by the cslom)
assign to

Mandatory Commands:
valid	- write all the mandatory cmds
invalid	- missing partial mandatory cmds
assign to	AO

Duplicate Commands:
valid	- get the list of commands that can be called more than once (with different parameters)
invalid	- duplicated commands with same parameters / - duplicate commands with different parameters
assign to	PE

Verilog Output:
valid	- check the csl verilog output
invalid
assign to	MH(for RF)

Format to Actual Mapping:
valid	- valid combinations with signal (multidim) groups and interface / - port to port connection / - signal to port connection / - interface to interface connection / - signal group to interface connection / - port to interface.port connection with different HID depth / - signal to interface.port connection with different HID depth / - ports to interface.port connections with ports with the same name but in different scopes / - signals to interface.port connections with ports with the same name but in different scopes / - get_signal to port connection ( v2.0) / - get_interface to port connection ( v2.0)
invalid	- invalid combinations with signal (multidim) groups and interface / - formal and actual ports have different sizes / - formal and actual interfaces have different sizes / - formal and actual interfaces have different structures / - signal has different size than port / - signal group has different structure than interface / - instance has more actual than formal parameters / - actual ports/ signals not defined / - actual interfaces/ signal groups not defined / - wrong names for implicit ports of register, register file, fifo, memory / - duplicate port mappings in actual parameters / - mapping that connect together two output ports / - mapping that connects an output port to an input port of same unit
assign to